## Slide 1: Introduction to Additive Manufacturing
Karl R. Haapala, Hari P.N. Nagarajan, and Amin Mirkouei
School of Mechanical, Industrial, and Manufacturing Engineering, Oregon State University

## Slide 2: Learning Outcomes
Understand the role of additive manufacturing processes in advanced manufacturing development
Learn to calculate the part build time in additive manufacturing

## Slide 3: Terminology
Advanced Manufacturing:
  “Use of innovative technologies to create existing products and the creation of new products. Advanced manufacturing can include production activities that depend on information, automation, computation, software, sensing, and networking.” (www.manufacturing.gov)
Additive Manufacturing (AM):
  American Society for Testing and Materials (ASTM) committee F42 defined additive manufacturing as “the process of joining materials to make objects from 3D model data, usually layer upon layer, as opposed to subtractive manufacturing methodologies.”

## Slide 4: Advanced Mfg. Needs & Challenges
Increase design flexibility / Reduce waste production
  Elimination of tooling and design constraints (e.g., fixtures & jigs)
Improve system flexibility / Reduce impact of manufacturing systems
  Elimination of work-in-process and stock obsolescence just-in-time manufacturing
Displacement of inefficient and detrimental processes
  Contributes to sustainability goals (i.e., economic, environmental, and social improvements)

## Slide 5: Additive Manufacturing
Layered manufacturing
Direct CAD manufacturing
Solid freeform fabrication
Rapid prototyping and manufacturing (RPM)
https://www.youtube.com/watch?v=cqhKYet6YBs
Notes: https://www.youtube.com/watch?v=cqhKYet6YBs

## Slide 6: Additive Manufacturing
A family of fabrication processes developed to make engineering prototypes with short lead time from a CAD model (hours or days)
Prototype machining may take up to several weeks
  Part complexity
  Difficulty in ordering materials

## Slide 7: Caterpillar Engine Mockup
200 parts made using stereolithography
Five weeks – produced, painted, assembled
Modified original CAD files
http://software.materialise.com/cases/materialise-magics-saves-caterpillar-huge-amounts-time

## Slide 8: What Materials Can We Print?
Thermoplastics, eutectic materials, edible materials, rubber, clay, metal clay, plaster, biomaterial
Ceramic materials, ceramic metal matrix composites
Photopolymers
Metal alloys (steel, iron, bronze, precious metals, titanium, cobalt, aluminum)
Paper, foil, plastic film
Source: Atre, 2015

## Slide 9: Additive Manufacturing Applications
Learning: answering questions about performance or feasibility
  e.g., proof-of-concept model
Communication: demonstration of a product for feedback
  e.g., 3D physical models of style or function
Integration: combination of sub-systems into system model
  e.g., alpha or beta test models
Milestones: development team’s schedule
  e.g., first testable hardware
Cranium replacement by Anatomics Powder-based binder jetting process
Source: http://www.wired.co.uk/

## Slide 10: Multiple Additive Manufacturing Approaches
Polymers
Metals
Alloys
Powders
Thermoplastics
Ceramics
Glass
Material
Stereolithography
Laser sintering
Laser melting
Selective laser melting
Fused deposition modeling
Electron beam melting
Binder jetting
Photopolymer jetting
Sheet lamination
Bioprinting
Technology
Automotive
Aerospace
Consumer
Medical
Industrial
Education
Application

## Slide 11: Additive Manufacturing Types
Liquid-based
  Liquid monomers that are cured layer by layer into solid polymers
Solid-based
  Solid sheets that are laminated to create the solid part
Powder-based
  Powders that are aggregated and bonded layer by layer

## Slide 12
https://www.linkedin.com/today/posts/noahfs

## Slide 13: Technology Summary Chart
Source: https://www.additively.com/en/learn-about/3d-printing-technologies

## Slide 14: Limitations of Additive Manufacturing
Strength Surface Finish Speed Cost
Improvements in surface finish
Increase in detail rendition by thinner layers
Improvements of material properties and range
Elimination of rework
Cut down of construction time
Reduce the total cost
Improvements
Notes:   Thermal properties
http://www.lynnesantiagolmhc.com/individual_therapy.html
Crescere fra palcoscenico e realtà on emazewww.emaze.com472 × 319Search by image

## Slide 15: Making a Prototype Part Using Additive Manufacturing
Create a CAD model
Export CAD model as .STL file
Import to AM software for pre-processing
  Tessellation: CAD model converted into a computerized format that approximates its surfaces by facets (triangles or polygons)
  Slicing of the model into layers: computerized model is sliced into closely-spaced parallel horizontal layers
Download to AM machine and make the part
Post process the part (process dependent)
Design 3D Model
Generate .STL File
Input File
Print
Part
Post
Process

## Slide 16: Making a Prototype Part Using Additive Manufacturing
http://www.davidbiles.co.uk/graphics/3d%20printing.png

## Slide 17: Part Build Time in Additive Manufacturing
Time to complete a single layer
Where:
  Ti = time to complete layer i
  Ai = area of layer i
  v = average scanning speed of the beam
  D = width of the extrudate deposited
  Td = delay time between layers
Can be applied to SLA and other AM processes with adaptation
  Amini, 2014, Time Estimation For Additive Manufacturing, M.S. Thesis, Texas State University, https://digital.library.txstate.edu/bitstream/handle/10877/5353/AMINI-THESIS-2014.pdf?sequence=1, accessed July 1, 2016.

## Slide 18: Part Build Time - continued
Once the Ti values have been determined for each layer (i), the build cycle time is:
Where:
  TC = build cycle time
  ni = number of layers used to approximate the part
Time to build a part ranges from one hour for small parts of simple geometry up to several dozen hours for complex parts

## Slide 19: Example
A prototype of a tube with a square cross-section is to be fabricated using fused deposition modeling.
  Outside dimension of the square = 100 mm
  Inside dimension = 90 mm (wall thickness = 5 mm except at corners)
  Height of the tube (z-direction) = 75 mm
  Layer thickness = 2.5 mm per layer
  Width of the extrudate deposited = 1.25 mm
  Extruder head is moved across in the x-y plane at a velocity of 150 mm/s.
Compute an estimate for the time required to build the part per minutes, if 10 s are lost each layer to lower the height of the platform that holds the part. (Neglect the time for post-curing.)

## Slide 20: Solution
Layer area Ai same for all layers.
Ai = 1002 – 902 = 1900 mm2
Time to complete one layer Ti is the same for all layers.
Ti = (1900 mm2)/(1.25 mm)(150 mm/s) + 10 s = 10.1 + 10 = 20.1 s
Number of layers
ni = (75 mm)/(2.5 mm/layer) = 30 layers
Build time
Tc = (30 layers)(20.1 s/layer) = 603 s = 10.05 minutes

## Slide 21: Closing Thoughts
National Interests and Manufacturing Needs
Advanced Manufacturing
Additive Manufacturing
Part Build Time in FDM
Traditional Manufacturing
Additive Manufacturing
http://www.thefabricator.com/news/shopmanagement/trumpf-enters-joint-venture-for-3-d-printing
http://westbaytech.com/machining.htm

## Slide 22: References
Groover, M.P., 2007, Fundamentals of Modern Manufacturing: Materials, Processes, and Systems, 3rd Ed., John Wiley & Sons, Hoboken, NJ.