## Slide 1: Additive Manufacturing Energy Modeling
Karl R. Haapala, Hari P.N. Nagarajan, and Amin Mirkouei
School of Mechanical, Industrial, and Manufacturing Engineering, Oregon State University

## Slide 2: Learning Outcomes
Understand the importance of energy evaluation of a process.
Analyze the energy and cost of producing a part using additive manufacturing process.

## Slide 3: Introduction
Prosperity
Food
Education
Water
Security
Health
Energy
Environment
Space
Global Grand Challenges
http://singularityu.org/global-grand-challenges/
Disaster Resilience
Governance
Notes: Awareness of Energy as a poignant factor of climate change is widespread.
“Energy is connected with key challenges such as climate change, environmental degradation, security, poverty, health, food production, agriculture, and water resources.”
Lund, 2015 (http://onlinelibrary.wiley.com/doi/10.1002/gch2.1001/pdf)

## Slide 4: U.S. Energy Consumption by Sector
Chart: 
| Residential | Commercial | Transportation | Industrial
 | 22 | 19 | 29 | 30
Source: EIA 2010
Notes: U.S. manufacturing sector consumes over one quarter of all U.S. energy use. [EIA 2010]
“Manufacturing Energy Consumption Survey (MECS) - U.S. Energy Information Administration (EIA).” Available: http://www.eia.gov/consumption/manufacturing/.

## Slide 5
Source: LLNL, 2016
Notes: https://flowcharts.llnl.gov/
A single energy flow chart depicting resources and their use represents vast quantities of data. Energy resources included solar, nuclear, hydroelectric, wind, geothermal, natural gas, coal, biomass, and petroleum. Energy flow diagrams change over time as new technologies are developed and as priorities change.

## Slide 6
Notes: Manufacturing contributes a significant portion of green house gases (GHG) emitted in the US and globally.

## Slide 7
Source: US DOE
Notes: “Manufacturing Energy Consumption Survey (MECS) - U.S. Energy Information Administration (EIA).” Available: http://www.eia.gov/consumption/manufacturing/.
Manufacturing energy and carbon footprint = 580 MMT CO2e = 10% U.S
A continuation to previous slide to show manufacturing as a significant contributor to greenhouse gas emissions

## Slide 8: Manufacturing Energy Trends
Chart: MECS Survey Year and Total Consumption for All Purposes
| 1991 | 1994 | 1998 | 2002 | 2006 | 2010
Net Electricity | 2370 | 2656 | 3035 | 2839 | 2851 | 2490
Natural Gas | 6095 | 6835 | 7426 | 6468 | 5911 | 5803
Coal and Coal Coke | 2314 | 2554 | 2275 | 2341 | 1705 | 1565
Fuel Oil and LPG | 2174 | 2279 | 2430 | 3477 | 2833 | 2368
Other | 6744 | 7339 | 8631 | 7541 | 7798 | 6836
(EIA 2010)
Notes: Traditional manufacturing energy use largely considered inconsequential until later half of 20th century.
Graph shows manufacturing energy trend. The energy trend starts to reduce around year 2000 when energy efficiency in manufacturing became of interest. The manufacturing energy use declined 17% from year 2000-2010. https://www.eia.gov/consumption/manufacturing/reports/2010/decrease_use.cfm
“Manufacturing Energy Consumption Survey (MECS) - U.S. Energy Information Administration (EIA).” Available: http://www.eia.gov/consumption/manufacturing/.

## Slide 9: Perspective of Process Energy and Embodied Energy
Process Energy
Material Embodied Energy
Notes: Manufacturing process (e.g., additive manufacturing) energy use is divided into process energy and material embedded energy. The process energy is small when compared to energy embodied (used in upstream processes) by the material. Material embodied energy is hidden and not considered in many energy studies.

## Slide 10: AM Energy Consumption Issues
Manufacturers produce products from primary material (polymers, ceramics, metals and composites).
  Direct Energy is used for plant operations in the form of electricity and fossil fuel use.
  Indirect energy use through embodied energy in primary materials.
  Energy use is product dependent.
Need to map the distribution of energy across the life cycle stages of the product.
AM
Infant Sector
More impact by optimizing
the development curve

## Slide 11: Energy: Design-Manufacturing
How does design and manufacturing impact energy consumption ?
  Material selection
    Application
    Geometry
  Process/parameter selection
    Materials
    Application and geometry
(Source: Vimeo)
(Source: Flickr)
Notes: https://c2.staticflickr.com/4/3828/19916773638_14dfe6fbb5_b.jpg
http://i.vimeocdn.com/video/553527400_1280x720.jpg

## Slide 12: AM Energy: Design-Manufacture
Requires understanding process inputs and outputs and their relationships

## Slide 13: Fused Deposition Modeling (FDM)
One of the most common additive manufacturing processes in the manufacturing sector.
Polymers: PLA, ABS, Nylon, PETE, HDPE, PC
Fills:
  Carbon Fiber; Graphite Glass Fiber
  Woods; Ceramics
  Metal Powders: Iron, Stainless steel, Bronze, Copper

## Slide 14: FDM Build Time
Build time
Post processing time
Part geometry
Total process time is the sum of build time and post-processing time.
Total Process Time: =
where:
  Tbuild is the part build time
  Tpost is the post-processing time
process characteristics & part geometry
dimensional size (x,y,z) & shape complexity (Sc)
part geometry

## Slide 15: FDM Build Time
Important parameters: Part height, part volume, part outside surface area, support height, support volume and base area
Build time of a process can be represented as a function of part surface area and part volume from experimental results through regression.
For an FDM process:
  where V is the volume of the part, and SA is the outside surface area of the part.
Notes: A design of experiments approach was used to identify the most important parameters that affected part build time.
For a sample size of 15, using step down regression, the part build time equation was formulated.

## Slide 16: FDM Post Processing Time (1)
Post-processing time (Tpost)
where,
tbase is the time to wash the base layer of support.
SA = part outside surface area
Ab = base outside surface area
Ni= number of internal channels
Ai = internal part surface area
K1,K2,K3 = degree of difficulty in washing
The degree of difficulty of washing can be calculated as:
  If Sc 1, K1 = 1, else K1 = 0
  If Sc 2, K2 = 1, else K2 = 0
  If Sc 3, K3 = 1, else K3 = 0
Shape complexity (Sc) is described next.

## Slide 17: FDM Post Processing Time (2)
The post processing time of the process depends on the shape complexity (Sc)
Shape complexity can be calculated as an index number based on part design conditions:
  Configuration: If the part design is 2.5D, then SC = 0; if the part design is 3D, then SC = 1.
  Aspect ratio: If part height/smallest cross-sectional size is < 10, then SC = 0, else SC =1.
  Feature scale ratio: If the triangle number (n)/volume is < 5000, then SC = 0, else SC = 1.
  Internal features: If the part has long, small channels or holes, then SC = 1, else SC = 0.
The overall shape complexity (Sc) is a summation of the four values above

## Slide 18: FDM Process Energy
Total Process Energy (Eprocess)
=
where
and where
PFDM is the rated power of the machine
Ppost is the rated power of part washing station

## Slide 19: Cost Analysis
The total cost of manufacturing a part using AM is the sum of material cost (Cmaterial), energy cost in the form electricity use (Cenergy), and labor cost (Clabor).
Material cost (Cmaterial)
  Where Cmodel is the cost of the model (part) material and Csupport is the support material cost.

## Slide 20: Cost Analysis
Cost of Model Material (Cmodel)
Cmodel = Vmodel cmodel
  where Vmodel is the volume of Model Material and cmodel is the Unit Cost of Model Material
Cost of Support Material (Csupport)
Csupport = Vsupport csupport
  where Vsupport is Volume of Support and csupport is the Unit Cost of Support Material
Total cost of energy (Cenergy) used in the form of electricity
Cenergy = Eprocess celectricty
  where Eprocess is Total Process Energy and celectricity is the Unit Cost of Electricity

## Slide 21: Cost Analysis
Total labor cost (Clabor)
Clabor = noperator W Tprocess
  where noperator is the number of operators, W is the operator hourly wage, and Tprocess is the total process time
Total product manufacturing cost (Cproduct)
Cproduct = Cmaterial Cenergy Clabor

## Slide 22: Example Problem
An automobile parts manufacturer wants to produce 1000 parts per month made of ABS material. The part is ring-shaped with a 1.0cm height, an outer diameter of 2.5cm and inner diameter 1.5cm.
The major cost drivers to fabricate the parts are material and energy use. Engineers have found the fused deposition modeling process build time is a major factor in reducing energy use. They developed the model below to calculate build time to manufacture one part as shown below (V is the volume of the part and SA is the surface area).
Calculate the total process energy and cost of manufacturing 1000 parts in an FDM machine with rated power of 22 kW.
The unit cost of ABS material = $45/kg. The density is 1.07 g/cm3
Assume no support material is used and no post processing is required

## Slide 23: Solution
The outer diameter of the part (D) = 2.5 cm
The inner diameter of the part (d) = 1.5 cm
The height of the part (h) = 1.0 cm
Volume of the part (V) = (π*(D2 – d2)*h)/4 = 3.925 cm3
The surface area of the part (SA) = π*(D-d)*h/2 = 1.57 cm2
The build time to manufacture one part (equation above for Tbuild) = 16 mins
The total build time = number of parts * Tbuild = (1000*16)/(60) = 266.7 hrs.
Machine energy use = rated power * total build time = 22*266.7 = 5867 kWh
The amount of ABS needed per part = density of ABS * part volume = 4.2 g
The total amount of material required = 4.2*1000 parts = 4200 g = 4.2 kg
Assuming $0.05/kWh for electricity, Total energy cost= 5867 * 0.05 = $293.35
Total material cost = 4.2*45 = $189

## Slide 24: Closing Thoughts
Translating the design and process parameter behavior into a process model can
  Reduce process variation due to infeasible parameter values
  Control process energy use from the early design stage
Energy analysis can
  Reduce undesirable processing time and energy costs associated with uninformed design decisions
  Allow designers to navigate the interrelationships between 3D CAD model data and process energy use

## Slide 25: Resources
Nagarajan, Hari PN, Harsha A. Malshe, Karl R. Haapala, and Yayue Pan. "Environmental Performance Evaluation of a Fast Mask Image Projection Stereolithography Process through Time and Energy Modeling." Journal of Manufacturing Science and Engineering (2016).
“Manufacturing Energy Consumption Survey (MECS) - U.S. Energy Information Administration (EIA).” Available: http://www.eia.gov/consumption/manufacturing.
“Additive Manufacturing and Sustainable Production for the 21st Century.” Econolyst: The 3D Printing & Additive Manufacturing People.
D. S. Thomas and S. W. Gilbert, “Costs and Cost Effectiveness of Additive Manufacturing,” National Institute of Standards and Technology, NIST SP 1176, Dec. 2014.