## Slide 1: Sustainable chemical process development
Early assessment of Economics, life cycle environmental impacts, Health and safety hazards
Dr. Akshay Patel

## Slide 2: Outline
Why?
Methodology
Data requirements
Case study
Case study inputs
Case study results
Summary
Case studies for homework

## Slide 3: The Challenge
Rapid Population growth (by 2050- 9 billion)
Consumption : Rich and emerging world
Inequity and poverty (environmental nexus)
  Climate change (CC) and other environmental problems
  Definite and insecure fossil resources
  Depletion of finite resources (metals, minerals)
  Degradation of renewable sources (forests, oceans, soil etc)

## Slide 4: Chemical manufacturing plant development
Chemical reactions
Chemical process engineering
Commercial plant operation
Plant design and installation
Notes: Multiple steps are involved in realizing a chemical manufacturing process. A variety of technology and business choices have to be made in each step which determine the characteristics (economic viability, safety, short and long term environmental impact, social impact, etc.) of the final manufacturing plant that goes into commercial operation.
The key is to understand what effect will your choice (e.g. of a catalyst or raw material or solvent) have on the world (system) in an objective manner. And use this understanding to make the right choices. Making the right choices is not just to meet the global challenges but in many cases they also determine whether the manufacturing facility can be realized in practice. (think about economic factors, regulations etc.)
This module is about making the right choices from a system perspective as we go through the multiple steps to design a manufacturing plant.

## Slide 5: System level characteristics
Economics
Life cycle environmental impacts
Social impacts
Regulations,
Business risks
Technical feasibility
Chemical process
Notes: Listed here are the key system level characteristics associated with a chemical manufacturing process. In this module you will learn about a methodological approach to rapidly understand the system effects of your choices. This approach enables you to rapidly iterate ideas so as to design a more sustainable chemical manufacturing process that can be realized in practice

## Slide 6: Process development & flexibility
Time
Flexibility
Information availability
Process concept
Laboratory experiments
Process design
Pilot trials
Commercial
production
Notes: As we go through the different stages of chemical process development, we make choices and fix things (e.g. selection of catalysts) which reduces our flexibility to make any changes so as to design a more sustainable facility. It is hence important to make the right choices very early on from a system level perspective.

## Slide 7: Early simulation of benefits & impacts
Process concept
Laboratory experiments
Process design
Pilot trials
Commercial
production
Early stage assessment (ESA)
Ex-ante sustainability assessment
Goals
Objective data-based sustainability assessment - Comparative
Faster feedback loop for sustainable process development
Rapidly analyze and identify promising process routes
Economy
Environment
Society
Detailed assessment (ESA)
Notes: The methodological approach that you will learn in this module is referred to as early stage assessment as it sits at the interface of chemistry and chemical engineering to enable better choices already early on in the chemical process development chain.

## Slide 8: Life cycle assessment basis
Systems overview
Avoid shifting burdens
Notes: To enable a system perspective, this methodological approach incorporates life cycle assessment methodology and combines the same with aspects of techno economic assessment, EHS assessment, business risk analysis and green chemistry. A chemical manufacturing facility is a link in the chain that starts from raw materials and goes towards recycling or waste treatment of end products. This whole chain exists in a wider global system. A systems perspective using life cycle assessment ensures that we make choices that help us to achieve a global optimum and avoid making choices which improve certain parts of the system to only shift the impacts/burden somewhere else in the chain. Think about using a safer solvent that can only be produced using a highly polluting process.

## Slide 9: Why do we develop a chemical manufacturing process
A chemical manufacturing process can be designed to meet any of the following demands:
  Find the best way to produce a certain product
  Find the best possible use for a raw material
  Find the best possible route to go from a specific raw material to a specific product
Polyethene
Ethanol
Butadiene
Naphtha
Monomers
SB rubber
AB rubber
Ethene
Propene

## Slide 10: Methodology
Conversion & Separation Process
Raw materials
Product/s
Reaction mass balance
Notes: At the core of a chemical manufacturing facility is a conversion process chemistry that plays a key role in addressing the demands. The choice of process chemistry will determine a variety of system level impacts associated with a chemical manufacturing facility. E.g. it determines which raw materials will be used or which solvents will be needed, etc. It is hence important to already make a good choice from a system level perspective when selecting a process chemistry. In this methodology, information about a process chemistry is coupled with quantitative and qualitative information to systematically take into account technical process engineering perspective and system level characteristics for a manufacturing process in a predictive manner. Hence, this methodology can be used by chemists to design an optimal process chemistry (e.g. a catalyst) and by chemical engineers to assess a large number of conversion process chemistry alternatives (e.g. different feedstocks, different catalysts) to select the best one for a manufacturing process.

## Slide 11: Methodology
Conversion & Separation Process
Raw materials
Product/s
Economics
Life cycle environmental impacts
Environment, Health and Safety aspects
External risks & benefits
Quantitative information
Reaction mass balance
Qualitative indicators
Notes: In this methodology , each process is evaluated based on 5 diff indicators that enable consideration of system level characteristics. The benefit of this approach is that it allows you to simultaneously consider all the factors and understand trade offs. E.g. a solvent can be cheaper but significantly more hazardous or the other way around.

## Slide 12: Methodology
Publication: Patel et. al (2012)
Notes: This figure shows an overview of the methodology and the parameters that go into the estimation of each indicator. The calculated values for each parameter are then combined in a multi-criteria evaluation using weights to derive a total score. In this methodology a new process is compared with its conventional counterpart that is subjected to similar evaluation. The comparison of these 2 processes leads us to an index ratio which gives a indication of the system level sustainability of the new process in comparison with the old process. The choice of the comparison process is important as that should very closely resemble the existing system of producing a particular product. Because with the new manufacturing facility you will be replacing the existing system. In case of completely new products one should look at the function that the new product fulfills and use a comparison counterpart for a product which fulfills the function in the existing system.

## Slide 13: Data
Chemical data
  Properties
  Prices and market information
  Life cycle impacts
  EHS hazards
Process data
  Reactor operating conditions
  Reaction mass balance
  Business and market risks
Notes: The methodology calculation is mainly based on:
Chemical data: Data on the chemicals involved in the conversion process
Process data: Data on the conversion process
The calculations based on the methodology are explained in detail in the reader text. These are also incorporated in the online tool.

## Slide 14: Case study
Butadiene production
Objectives
  Rapidly assess the feasibility and sustainability of a new biobased production route for 1,3-butadiene from ethanol.
  Understand and report on the uncertainties in your analysis and their effect on the outcome of your assessment
  Understand future scenarios dependent on market or societal trends and its effect on the outcome of your analysis
  Prepare a report and recommend next steps for the development (if at all) of the new technology
  Consider other alternatives for 1,3-butadiene production
Notes: In this case study we will look at the production of Butadiene and try to find a new sustainable manufacturing alternative to produce butadiene. As we go through the case study results we will take go deeper into the methodology to understand the specific calculations.

## Slide 15: Butadiene production
From Ethanol
From Naphtha
Economic constraint
Env. impact…
Process costs…
EHS Index
Risk aspects …
Total score
Existing commercially dominant process
Potentially new commercial process
Notes: Refer to the case study document for the case study data inputs. Both these processes are one reactor step processes. However, you using the online tool, you can also model multiple reactor and separation steps in a chain.

## Slide 16: Process data
Process data
  Reaction mass balance
Notes: Reaction/Reactor mass balance is the basic starting point for calculations. You can do a first assessment just based on a reaction stoichiometry and then if the process seems to work, then you should go about finding more detailed reactor mass balance information either from literature or own experiments.

## Slide 17: Economic constraint/Margin
Economic constraint = Allocated Raw material cost/Market price of product
Allocated Raw material cost = f (Practical yields, Market price of product and co-products, Raw material costs)
Economic allocation
Economic constraint
Env. impact…
Process costs…
EHS Index
Risk aspects …
Total score
Chart: Economic constraint
| Bioethanol-based | Naphtha-based
Economic constraint | 0.99734 | 0.82893
Notes: This factor is a basic consideration of the raw material costs as a fraction of the income that can be generated from selling the products and the co products. A EC value of more than 1 means the raw material costs will be higher than the income generated and hence leading to an economically unviable process.

## Slide 18: Economic constraint data input
Chemical data
  Prices of raw materials, products and co-products
  Consider time and regional variations
Notes: Refer to the reader text for more details regarding the calculations.

## Slide 19: Environmental impact of raw materials
Cumulative Energy Demand (CED) = f (Raw material CED, Practical yields, Market prices, Heating values)
GHG emissions = f (Raw material eq. CO2 emissions, Practical yields, Market prices)
Economic constraint
Env. impact…
Process costs…
EHS Index
Risk aspects …
Total score
Chart: MJ/kg but-1,3-diene
CED | 118.9605 | 61.174
GHG emissions | 2.4475 | 3.984
Notes: This factor considers the environmental impact based on the raw materials used in the process. Two key indicators of Cumulative Energy Demand and Green house gas emission are used to represent the life cycle environmental impacts.

## Slide 20: Env. Impact of raw mat. data input
Chemical data
  Raw materials
    Cumulative Energy Demand
    Greenhouse gas emissions
  Main-product
    Lower heating value
    Carbon content (kgCO2 eqv.)
Notes: The calculation for environmental impact also encompasses an allocation factor to fairly allocate the impacts between the main products and the co products. It is to avoid allocation of all or no impacts to the main product as that would lead to an unfair comparison which does not represent practical realities from a system perspective.

## Slide 21: Process cost and environmental impact
For chemical catalytic processes
  Presence of water
  Product concentration
  Boiling point difference
  Inherent reaction mass loss
  Reaction energy
  No. of co-products
  Feedstock Pre-treatment
Economic constraint
Env. impact…
Process costs…
EHS Index
Risk aspects …
Total score
Ref: Adapted from H. Sugiyama (2007)
Chart: 
| Bioethanol-based | Naphtha-based
Presence of water | 1 | 0
Product concentration | 0.047143 | 0.59837
Boiling point | 0 | 1
Inherent reaction mass loss | 0.38022 | 0
Reaction energy | 0 | 1
No. of co-products | 0.5 | 1
Pre-treatment | 0 | 0
Notes: Since we are doing an early stage assessment at the conversion process chemistry stage, it is important to consider the process engineering perspective which will enable us to estimate the costs and environmental impacts for the facility. Developing detailed process models for each and every process chemistry is not practically possible today (unless intelligently automated in future). Hence we use this semi quantitative indicator that predicts the process cost (including capital and non raw material operating costs) and environmental impacts using correlations that are based on heuristics and historical data.

## Slide 22: Process cost and environmental impact
For bio catalytic processes
  Downstream processing
    Type of metabolite
    Distillation requirement
    Need for complex separation alternatives
  Product concentration
  Boiling point difference (in case if distillation is needed)
  Inherent reaction mass loss
  Reaction energy
  No. of co-products
  Feedstock Pre-treatment
Economic constraint
Env. impact…
Process costs…
EHS Index
Risk aspects …
Total score
Ref: Moncada et. al (2015)
Notes: The PCEI calculation listed here has been developed by Moncada et al to specifically address biochemical processes. It includes additional factors for downstream processing that are specific to biochemical processes. The calculations for this are also incorporated in the online software module. However, the case study in this education module is focused on chemical catalytic route and hence this calculation is not used for the case study.

## Slide 23: PCEI data input
Process data
  Reactor output mass flows
  Reaction temperature
  Enthalpy change
  Feedstock pre-treatment (Qualitative input)
Chemical data
  Molecular weight
  Boiling point
Notes: Key data about the process and the chemicals involved is required for the estimation of PCEI. Refer to the reader text for more information on the calculations.

## Slide 24: EHS Index
Environmental hazard (0.4)
  Persistency
  Air hazard
  Water hazard
  Solid waste
Health hazard (0.2)
  Irritation
  Chronic toxicity
Safety hazard (0.4)
  Mobility
  Fire/explosion
  Reactivity
  Acute toxicity
Economic constraint
Env. impact…
EHS index
Process costs…
Risk aspects …
Total score
Ref: H. Sugiyama (2007)
Chart: EHS index
| Bioethanol-based | Naphtha-based
Hazard index | 1.9532 | 2.6721
Notes: Understanding the EHS characteristics of a chemical process can help us design a manufacturing process that is inherently safer. This can lead to significant cost savings over the whole life cycle of a manufacturing facility. Hence in this methodology we estimate these characteristics using EHS index in which various hazard indicators are estimated based on the hazard characteristics of the chemicals involved and their mass flows in the system. Refer to the reader text for more information on the calculations.

## Slide 25: EHS hazards data input
Chemical data: best case
  Boiling point
  Flash point
  NFPA reactivity
  EU classification
  R-codes (H codes)
  LC50 aquatic
  Half life (water)
  LD50dermal
  WGK
  Substance class
  IDLH
  Vapor pressure
Chemical data: acceptable
  Boiling point
  Flash point
  NFPA reactivity
  EU classification
  R-codes (H codes)
  LC50 aquatic
  Half life (water)
  LD50
  WGK
  Substance class
  IDLH
  Vapor pressure
Notes: Please refer to the reader text for further information on calculating each of these data inputs. Getting all the data that is listed here is not always possible and is also not always needed. Having data for the inputs highlighted in bold in the best case leads to the best possible results (considering priorities for data category preference). However, it is absolutely essential to have good data for the inputs highlighted in the acceptable case to have an acceptable EHS assessment.

## Slide 26: Risk aspects
Scores based on qualitative statements
Refining of scores based on results
Parameters
  Feedstock supply risk
  Market risk
  Infrastructure (availability) risk
  Regional feedstock availability
  Application-technical aspects
Economic constraint
Env. impact…
Macro risk…
Process costs…
EHS index
Total score
Chart: 
| Bioethanol-based | Naphtha-based
a | 0 | 0
b | 0 | 0
c | 0.066 | 0
d | 0 | 0.075
e | 0.075 | 0.075
Notes: A key aspect in deciding on a chemical process route is the business risk associated with a manufacturing facility. It is important to mitigate these risks so as to ensure practical realization of a manufacturing facility. Hence in this methodology we consider these risks using qualitative indicators that are determined based on scoring statements. Refer to the reader text for more information on the scoring for these indicators.

## Slide 27: Risk aspects data input
Process data
  Qualitative scores for risk aspects
Notes: Refer to the reader text for more information on the specific data inputs needed for assessing risk aspects.

## Slide 28: Assessment Boundary
Notes: In this early stage assessment, we combine quantitative and qualitative aspects. To ensure a higher quality of output it is important to base the analysis on as much quantitative data as possible. So essentially to minimize the use of PCEI indicator for only the stage where quantitative data on inputs in not available. In this case study we had information on prices, CED, GHG for ethanol and hence we only had to take into consideration one conversion step from ethanol to butadiene.

## Slide 29: Assessment Boundary
Notes: However, if we did not have good data on ethanol then we could go further back in the chain and base our analysis on the quantitative data for glucose. And for the two steps from glucose we use the estimation of the process provided by PCEI.

## Slide 30: Integrated results
Index Ratio = 0.90
Bioethanol Score / Naphtha score
Economic constraint…
Env. impact…
Total score/Ind.
Process costs…
Risk aspects …
EHS index
Chart: Index ratio
| Bioethanol-based | Naphtha-based
Economic constraint (0.3) | 0.3 | 0.24934
Env. impact of raw materials (0.2) | 0.16143 | 0.15142
Process costs and env. impacts (0.2) | 0.10712 | 0.2
EHS hazard (0.2) | 0.14619 | 0.2
Risk aspects (0.1) | 0.094 | 0.1
Lower scores are better
Notes: The integrated results include normalization of the calculated scores for each indicator and weighing. This is an important step that goes into the direction on combining the analysis that we have done so far, for decision making purposes. Ideally a new process should be better (lower scores) on all the parameters, however that is seldom the case and hence we use weighting factors to weight the parameters to take a decision. Refer to the reader text for detailed reasoning and calculation steps. The index ratio is merely a division on the total scores of both the processes that we are comparing. In this case a lower index ratio would mean that the new bioethanol based process might be favorable under the conditions that we have selected. A single indicator makes it easy to take a decision and more importantly enables the use of decision support analysis such as sensitivity, uncertainty and scenarios.

## Slide 31: Sensitivity analysis
Sensitivity analysis allows us to understand the sensitivity of the outcome to changes in specific data inputs.
Exercise: In the above example study and report on the sensitivity of the final index ratio to a 20% decrease in the price of ethanol.

## Slide 32: Uncertainty analysis (data inputs)
Env. impact…
Index ratio
Process costs…
Risk aspects …
EHS index
Economic constraint…
Chart: 
Default1 | 0
Default2
meanLabel | 0
xDelimiter | 0 | 0
Notes: As opposed to sensitivity analysis and uncertainty analysis is basically variation in a whole lot of data inputs with an additional information about the probability of which variations are expected to occur with a higher probability as compared to others. Understanding the effect of uncertainties is important is it helps us to determine the robustness of the outcome and take a decision. In this above example most of the outcomes indicate that the new process can be better as compared to the existing process. However, there are some situations (less probable) in which the existing process might be better.

## Slide 33: Uncertainty analysis (weights)
Env. impact…
Index ratio
Process costs…
Risk aspects …
EHS index
Chart: Count
| 0.79188332367320979 | 0.79902225280449668 | 0.80616118193577957 | 0.81330011106706546 | 0.82043904019835068 | 0.82757796932963557 | 0.83471689846092112 | 0.84185582759220801 | 0.84899475672349489 | 0.85613368585477678 | 0.863272614986062 | 0.87041154411734656 | 0.87755047324863411 | 0.88468940237991911 | 0.89182833151120289 | 0.89896726064248811 | 0.90610618977377189 | 0.91324511890505855 | 0.92038404803634233 | 0.92752297716762755 | 0.93466190629891566 | 0.94180083543020121 | 0.94893976456148565 | 0.95607869369277243 | 0.9632176228240551 | 0.97035655195533876 | 0.97749548108662554 | 0.98463441021791076 | 0.99177333934919665 | 0.9989122684804812 | 1.0060511976117663 | 1.0131901267430521 | 1.0203290558743328 | 1.0274679850056216 | 1.0346069141369081 | 1.0417458432681919 | 1.0488847723994732 | 1.0560237015307621 | 1.0631626306620472 | 1.0703015597933323 | 1.0774404889246174
BarChart | 1 | 0 | 0 | 1 | 1 | 6 | 14 | 14 | 24 | 25 | 41 | 52 | 48 | 49 | 53 | 50 | 54 | 44 | 49 | 50 | 49 | 44 | 50 | 38 | 32 | 46 | 22 | 29 | 23 | 14 | 17 | 12 | 10 | 11 | 5 | 5 | 4 | 4 | 6 | 1 | 2
Economic constraint…
Notes: A similar logic can also be applied to weights.

## Slide 34: Sustainable process development
Multi-criteria approach
Feedback loop
Chart: 
| 301
Bottom | 0.9741
Notes: With this early stage approach we incorporate multiple criteria such as economics, safety, life cycle environmental impact in developing a new chemical process. The key benefit is that the early stage multi criteria approach enables a rapid feedback loop that can lead to the design and development of sustainable production routes. Thinkabout using the feedback loop to develop new catalysts.

## Slide 35: Future scenarios
Uncertainty analysis provides a general idea about the expected variation in output.
However, many times we would also like to know how our assessment would be in a particular future scenario.
An example in this case is the availability of lignocellulosic ethanol in near future or carbon taxes or the development of a more efficient catalyst to convert ethanol into butadiene.
Exercise: Assess the outcome for a future scenario in which lignocellulosic ethanol with a price of 650 USD/metric tonne, CED of 48 MJ/kg ethanol and GHG emissions of - 0.219 kgCO2 eq./kg ethanol is available.
Publication: Early-stage comparative sustainability assessment of novel biobased processes, A.D. Patel, K. Meesters, H. den Uil, E. De Jong, E Worrell, M.K. Patel, ChemSusChem, 2013, 6 (9), 1724-1736

## Slide 36: Report
Why did you select these process/es for assessment?
  E.g. Market demands for sustainable biobased alternatives
Comments on the completeness of the data?
  Do you miss some data or is the time and region not appropriate
Are there any particular red-flags?
  E.g. Unfeasible economic margin (>2)
What was your reasoning behind the weighting factors (If you would recommend taking a decision based on overall score)?
Based on the data and outcomes which process would you recommend and why?
  E.g. Sensitivity and trends
What follow up actions do you recommend?
  E.g. Experiments, Re-evaluation at a later date or circumstances
Notes: Use this points to create a report for your case study

## Slide 37: Acknowledgement
This module has been funded with a grant from NSF

## Slide 38
Thank you
Akshay Patel
+31 (0) 30 8080139
adpatel@sustanalyze.com
www.sustanalyze.com
Utrecht Science Park
Padualaan 8, 3584CH
Utrecht, the Netherlands

## Slide 39
Extra slides

## Slide 40: EHS: Environment

## Slide 41: EHS: Health

## Slide 42: EHS: Safety