## Slide 1: Green Process Design Application of Green Chemistry to Manufacture Specialty Chemicals from Renewable Resources Case Study Overview
© 2013 J.R. Seay / University of Kentucky. For educational use only. Do not copy.
Notes: Copyright Note: All clip art images and photographs in this document are the work of others and claimed under Academic Fair Use provisions of U.S. Copyright Law.
Jeffrey R. Seay, PhD, PE
Assistant Professor of Chemical and Materials Engineering
University of Kentucky College of Engineering, Paducah Extended Campus
Dr. Seay joined the University of Kentucky after a 12 year industry career in process design, project management and process safety. Dr. Seay is also a participating faculty in the Institute for Sustainable Manufacturing at the University of Kentucky. He has previously served as the Chair of the Education Committee of the AIChE Sustainable Engineering Forum (SEF) and is the current Vice-Chair. He has co-authored numerous peer-reviewed papers on sustainable chemical engineering education and is the inaugural recipient for the SEF Education Award. Dr. Seay teaches a sustainability focused elective course at the University of Kentucky and has extensive experience in sustainability renewable energy education.

## Slide 2: Module Learning Objectives
Upon the completion of this module, participants should:
  Be aware of the three pillars of Sustainability
  Understand how the 12 Principles of Green Chemistry can be used to guide process design decisions.
  Be aware of the potential benefits of utilizing renewable feedstocks as opposed to petroleum based feedstocks.
  Understand background of the US EPA Waste Reduction (WAR) Algorithm.
  Be aware of the appropriate usage of the WAR Algorithm, and understand when it cannot be applied.
  Understand what a Life Cycle Assessment (LCA) for a chemical product or process encompasses.
  Be aware of why LCA is an important tool for assessing the impacts of a product or process.
Notes: This module is designed for students from the sophomore level to the senior level. Objectives can be adjusted by the course instructor to fit the individual needs of the students.

## Slide 3: Overview – Questions for Consideration
How does green chemistry influence our approach to process design?
How can Chemical Engineers use the 12 Principles of Green Chemistry to design sustainable process?
What are the potential benefits of switching to renewable chemical feedstocks?
How can we assess the potential benefits of switching to green chemistry based processes?
What skills and tools are needed to design and assess processes based on green chemistry?
Notes: These questions can serve as the basis for in-class discussion. The questions are intended to get students thinking about how we can determine if a process is really “green” or “sustainable”. At this point, the students shouldn’t have concrete answers, but rather should be thinking about what might be needed to answer the questions posed.
This is a good time to administer the pre-course assessment test provided with the module.

## Slide 4: Overview of Sustainability
Notes: This section will provide general background on the meaning and recent history of sustainability.

## Slide 5: A Short History of Sustainability
Bruntland Commission
  “Sustainable development is development that meets the needs of the present without compromising the ability of future generations to meet their own needs.”
Rio Conference
  Held in 1992. Led to the formation of the UN Commission on Sustainable Development, which eventually led to the Kyoto Protocol.
So what does this mean for engineers???
Notes: The World Commission on Environment and Development, commonly called the Bruntland Commission, issued a report, published in 1987, in a book titled “Our Common Future” (Brunland, 1987).
Although there is no single accepted definition of the term sustainability, the Bruntland Commission definition of sustainable development forms the basis of what sustainability means to the field of engineering.
For design engineers in particular, sustainability has come to refer to the goal of designing, operating and maintaining products and processes in a manner that is economically viable, environmentally benign, and beneficial to society.
In other words, a sustainable process or product is one that is designed, operated and maintained to meet the triple bottom line of economics, environment and society, both now and in the future.

## Slide 6: So What is Sustainability?
Unfortunately there isn’t one single accepted definition of sustainability.
However, most agree that for a process or product to be sustainable it must meet three criteria:
  Economically Sustainable
  Environmentally Sustainable
  Socially Sustainable
These three aspects are not always in agreement!
Notes: In sustainability, we often talk about the “Triple Bottom Line” of Economics, Society and the Environment. Our goal in sustainable product and process design is therefore is to develop products and processes that are optimized to consider each of these goals.
Even if we don’t achieve peak performance in any one single aspect, our designs are optimized to get the highest performance when considering all three.

## Slide 7: The Triple Bottom Line
Triple Bottom Line
  Economy
  Environment
  Society
Economic Sustainability
  A sustainable economy is one in which the ability to generate income (profit) is maintained.
Environmental and Societal Sustainability are harder to define.
  Key point of most definitions is the concept of sustainability now, and in the future.
  “Intergenerational Equity”
Notes: Sustainability is really all about optimizing. Instead of only focusing on one area (bottom line), we consider three. We know that products that aren’t profitable won’t get manufactured and processes that aren’t profitable won’t get built, but in addition to being profitable, we argue that products are processes must not do irreparable harm to the environment and must be beneficial to society.
Societal sustainability is harder to quantify. Clearly people need jobs and the income they provide, but should our health or safety be compromised in the process? These are the types of questions we have to answer in order to be sustainable. Throughout this module, we will take a look at some of the engineering tools we have at our disposal to try to answer these questions.
Intergenerational Equity can be a tricky concept. It doesn’t necessarily mean that we must leave specific resources (like oil) to future generations, but we must leave the capacity for future generations to meet their own needs.

## Slide 8: What’s the Difference Between Sustainability and Green Engineering?
Society
Economy
Environment
Green Engineering
Sustainability
Notes: The fields of Sustainability and Green Engineering are closely related. Green Engineering is an important part of sustainability, however, the goal of sustainable design is find the optimum process and product designs that benefit society and are economically viable, in addition to being environmentally friendly.
A sustainable design is one that provides benefit to all three sectors.

## Slide 9: Overview of Green Chemistry
Notes: This section of the module will provide an overview of what green chemistry means, and define the 12 principles of green chemistry.

## Slide 10: A Bit of History
In the early days of the chemical industry, the design team basically consisted of a Research Chemist and Mechanical Engineer.
The Mechanical Engineer’s job was basically to recreate the chemist’s lab on a larger scale.
The industry evolved this way due to its heritage in the specialty dye industry.
Later, the chemical industry realized the need to produce commodity chemicals.
In other words, making large quantities of only a few chemicals.
This led to the Unit Operations approach to process design.
Notes: These two approaches have led to inflexibility. The research chemist approach is limited by inflexibility in equipment design and configuration and the Unit Operations approach leads to a loss of the “big picture” of the process design. As a result of this, engineers recognized the need for a systems approach to process design. This led to the development of a Design Heuristic approach process design.

## Slide 11: Green Chemistry and Process Design
Green Chemistry is a Design Methodology based on a series of Heuristics.
These heuristics are analogous to other methodologies you may be familiar with:
  Inherently Safe Process Design
  Design for Optimum Recycle
  Design for Pollution Prevention (remember the PPA)
The purpose of this methodology is to guide the design engineer / research chemist during the initial discovery phase of process design.
This can be illustrated by the use of a graph.
Notes: Heuristics often come down to common sense. Heuristics based on Green Chemistry are no different – they may appear obvious, but there is value in documenting and formalizing the process.

## Slide 12: Capital Projects and the Process Engineer
As we have seen in the previous module, the process engineer has the most influence on the process outcome in the earliest stages of a capital project.
Notes: Clearly, the engineer’s ability to reduce cost is greatest in the earliest stages of process design. This idea is fairly obvious. An analogy can be made to environmentally conscious design as well. The engineer’s greatest opportunity the influence the environmental performance of the process is at the beginning as well.
Although “end of the pipe” strategies can always be employed later, the inherent environmental performance is often decided in the early stages of design.

## Slide 13: 12 Principles of Green Chemistry
Notes: These principles were developed by Anastas and Warner for the US EPA. The EPA now sponsors an award for innovations in green chemistry.

## Slide 14: Chemical Route Selection
Chemical products can be produced by a variety of synthesis routes.
Different routes of course have different results in terms of cost, energy usage, life-cycle impacts and potential environmental impacts.
Of course, we will later learn how to evaluate these impacts in a quantitative manner.
However, we often need a place to start with regard to route selection.
This is where the design heuristic called “The 12 Principles of Green Chemistry” comes in.
Notes: The 12 Principles of Green Chemistry provide a framework for making design decisions during the discovery phase of a capital project.
In general, the 12 Principles address:
Alternative Feedstocks
Green Solvents
Synthesis Pathways
Inherently Safer Chemistry

## Slide 15: 12 Principles of Green Chemistry
Prevention
  It is better to prevent waste than to treat or clean up waste after it has been created.
Atom Economy
  Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
Less Hazardous Chemical Syntheses
  Wherever practicable, synthetic methods should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
Designing Safer Chemicals
  Chemical products should be designed to effect their desired function while minimizing their toxicity.
Notes: Principles 1 - 4

## Slide 16: 12 Principles of Green Chemistry - Continued
Safer Solvents and Auxiliaries
  The use of auxiliary substances (e.g., solvents, separation agents, etc.) should be made unnecessary wherever possible and innocuous when used.
Design for Energy Efficiency
  Energy requirements of chemical processes should be recognized for their environmental and economic impacts and should be minimized. If possible, synthetic methods should be conducted at ambient temperature and pressure.
Use of Renewable Feedstocks
  A raw material or feedstock should be renewable rather than depleting whenever technically and economically practicable.
Reduce Derivatives
  Unnecessary derivatization (use of blocking groups, protection/ deprotection, temporary modification of physical/chemical processes) should be minimized or avoided if possible, because such steps require additional reagents and can generate waste.
Notes: Principles 5 - 8

## Slide 17: 12 Principles of Green Chemistry - Continued
Catalysis
  Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
Design for Degradation
  Chemical products should be designed so that at the end of their function they break down into innocuous degradation products and do not persist in the environment.
Real-time analysis for Pollution Prevention
  Analytical methodologies need to be further developed to allow for real-time, in-process monitoring and control prior to the formation of hazardous substances.
Inherently Safer Chemistry for Accident Prevention
  Substances and the form of a substance used in a chemical process should be chosen to minimize the potential for chemical accidents, including releases, explosions, and fires.
* Anastas, P. T.; Warner, J. C.; Green Chemistry: Theory and Practice, Oxford University Press: New York, 1998.
Notes: Principles 9 - 12

## Slide 18: But What About Chemical Engineering?
Of course, these heuristics must be put into the context of conceptual process design.
As we have seen, processes that appear green may not be when we consider the entire lifecycle.
Sometimes things begin to fall apart when we consider the entire process design, beyond just the reactor.
Sometimes a greener solvent may lead to a more difficult separation, which would require additional energy.
In other words…
As engineers, we are uniquely qualified to take a systems view, realizing that the object of our optimization changes based on our unique situation.
Notes: These principles generally only address the chemistry of a process (note that they are not called the 12 Principles of Green Engineering)

## Slide 19: Green Chemistry Based Design Case Study
Notes: This section of the module material covers the background and basis for the green chemistry case study presented in this module. The case study will be used in the Inquiry Activity included in this module.

## Slide 20: The Growing U.S. Biodiesel Market
Page | 20
Figure Reference: 2012 BP Statistical Review of World Energy
Notes: Recent trends and tax incentives indicate a potential for growth in the biodiesel market.
Although there remains significant debate regarding the role biodesel will play regarding the future of American energy policy, it is clearly a growing industry.
Biodiesel is produced from renewable feedstocks. However, with any sustainable process, we must take a broader look that encompasses the entire product life cycle to determine the real impact on the environment and on the overall carbon utilization of this alternative fuel source.
While initially concentrated in the Midwest, Biodiesel production facilities are now found across the country.

## Slide 21: Biodiesel Lifecycle Flowchart
Page | 21
Biodiesel is an alternative to petroleum diesel produced from agricultural products.
In order for the process to be sustainable, uses must be found for the process byproducts.
*Reference: Rene Elms, TAMU, 2007
Notes: Life Cycle Assessment (LCA) is defined as studying “the environmental aspects and potential impacts of a product or process or service throughout its life, from raw material acquisition through production, use and disposal” (ISO, 1997).
Thus, when considering the sustainability of a process, the entire supply must be considered. The step this is of particular interest for my research is the generation of Glycerol, which is a byproduct of biodiesel manufacturing.
For every 9 kg of biodiesel produced, 1 kg of crude glycerol is formed as a side product.
Finding an industrial use for this glycerol improves the carbon utilization and economic viability of the biodiesel process.

## Slide 22: Case Study Background
Many well established chemical products and intermediates, currently produced from Propylene, can also be produced from bio-based Glycerol.
    Acrylic Acid
    1,3-Propanediol
    Acrolein
Recent emphasis of global climate change and sustainability make switching production from crude oil derived to renewable raw materials attractive.
Additionally, using Glycerol produced as side product of biodiesel production potentially enhances the overall carbon utilization of the biodiesel process.
Development of an industrial process based on Glycerol dehydration chemistry, and the comparison of this process with the traditional, Propylene based process.
Case Study Focus
Page | 22
Notes: Glycerol is a sustainable, biobased feed source for C3 chemistry.
Other products include, Propionaldehyde, 1,2-Propanediol, Acetone among Hydroxyacetone others

## Slide 23: Glycerol Dehydration Pathways
The Glycerol dehydration reaction is catalyzed by Phosphoric Acid supported on silica.
In the first reaction step, Glycerol is dehydrated to Hydroxyacetone and 3-Hydroxypropionaldehyde.
3-Hydroxypropionaldehyde can dehydrate to produce Acrolein or decompose to Acetaldehyde and Formaldehyde.
No Hydrogen or Oxygen is present in the feed, limiting side reaction products.
Page | 23
Notes: This list of reactions is not comprehensive, but illustrates the pathways to produce chemicals of industrial importance.
Acrolein is the focus of this case study. Acrolein is an important feed stock in the production of the essential amino acid Methionine.

## Slide 24: Propylene Based Process
Vaporized Propylene and air are fed to a shell and tube packed bed reactor.
Propylene is converted to Acrolein via catalytic partial oxidation at low pressure.
The reaction is highly exothermic and is cooled by circulating molten salt heat transfer fluid.
Water quenching and absorption – desorption separate Acrolein from the reactor effluent.
The remaining vent gas, is compressed and recycled back to the reactor.
Traditional Production Process
Page | 24
Notes: In order to assess the viability of a glycerol based process, a model of the industry standard propylene process is required. Pay special attention to the separation train – we will see this again on the next slide when we review the glycerol based process.

## Slide 25: Green Chemistry Based Process
Glycerol Based Process
Page | 25
The Inert Gas Process is based on replacing the water used to dilute the Glycerol feed with Nitrogen.
Reaction conditions are similar to the Vapor Phase Glycerol process.
Since Nitrogen is used instead of water, the separation train is identical to the traditional Propylene process.
The Inert Gas Process has an energy advantage over the Vapor Phase Process due to minimizing the vaporization of dilution water.
Notes: This process is important not only because it addresses the high energy cost of converting glycerol to acrolein, but it’ similar to the propylene process. Having a similar process is important for retrofitting existing acrolein production facilities. As noted on the last slide, the separation train is based on the established technology of the propylene process.

## Slide 26: Comparing the Two Processes
Traditional Process
  Exothermic reaction allow steam production from recovered heat
  Established technology
  Process safety concerns due to runaway reaction and use of liquefied propylene feedstock
  Non-renewable feedstock
Green Chemistry Process
  Endothermic reaction puts the process at an energy disadvantage
  However, endothermic reaction is inherently safer
  New, unproven technology
  Renewable feedstock produced from a waste product
  Potential for process integration with biodiesel production process
Notes: It’s important to note that, to date, the Green Chemistry process has not been implemented on an industrial basis. However, the process is viable so it can be easily compared with the traditional, propylene process.

## Slide 27: Considering the 12 Principles of Green Chemistry
Prevention
Atom Economy
Less Hazardous Chemical Syntheses
Designing Safer Chemicals
Safer Solvents and Auxiliaries
Design for Energy Efficiency
Use of Renewable Feedstocks
Reduce Derivatives
Catalysis
Design for Degradation
Real-time analysis for Pollution Prevention
Inherently Safer Chemistry for Accident Prevention
Notes: The principles highlighted in green are specifically addressed by the proposed “Green Chemistry” process.

## Slide 28: Assessing Environmental Impacts
Notes: First we will spend a few minutes describing why we need Environmental Impact Assessment.

## Slide 29: A Little Bit of Background The Waste Reduction (WAR) Algorithm
Notes: This material based on:
Young, Douglas, Richard Scharp and Heriberto Cabezas (2000): “The waste reduction (WAR) algorithm: environmental impacts, energy consumption, and engineering economics”, Waste Management, Vol. 20.

## Slide 30: Regulatory Background
The Pollution Prevention Act of 1990 established a national policy that pollution should be prevented or reduced at its source.
The act also directed EPA to develop and implement a strategy promoting source reduction, which it defined as any practice that reduces:
  (1) the amount of any hazardous substance, pollutant, or contaminant from entering any waste stream or being released into the environment prior to recycling, treatment, or disposal, and
  (2) the hazards to public health and the environment associated with the release. These measures can range from simple techniques, such as covering exposed containers of volatile organic compounds or tightening loose pipe connections, to completely redesigning a production process or reformulating a product.
Notes: Under the act, pollution that cannot be prevented should be recycled or treated in a safe manner; disposal or other releases should be used only as a last resort. This is aimed at preventing “end of the pipe” abatement strategies and focuses instead on preventing pollution at its source.

## Slide 31: Waste Minimization Research at the U.S. EPA
Overview of Research in Clean Processes at the EPA:
  http://www.epa.gov/nrmrl/std/cppb/index.html
Notes: You will find many useful resources here…

## Slide 32: A New Assessment Tool
In traditional chemical process design, attention is focused primarily upon minimizing cost, while the environmental impact of a process is often overlooked.
This may in many instances lead to the production of large quantities of waste materials. It is possible to reduce the generation of these wastes and their environmental impact by modifying the design of the process.
However, the design methodologies for waste minimization do not exist, and, thus, research activities have been underway at EPA's National Risk Management Research Laboratory to develop such methodologies.
Notes: All data and information in the following slides from the U.S. EPA website.

## Slide 33: Basis of the Assessment Methodology
The method is based on a potential environmental impact (PEI) balance for chemical processes.
The PEI is a relative measure of the potential for a chemical to have an adverse effect on human health and the environment (e.g., aquatic ecotoxicolgy, global warming, etc.).
The result of the PEI balance is an impact (pollution) index that provides a quantitative measure of the impact of the waste generated in the process.
The goal of this methodology is to minimize the PEI for a process instead of minimizing the amount of waste (pollutants) generated by a process.

## Slide 34: WAR Algorithm - Theory
Contains material adapted from:
Young, Douglas, Richard Scharp and Heriberto Cabezas (2000): “The waste reduction (WAR) algorithm: environmental impacts, energy consumption, and engineering economics”, Waste Management, Vol. 20.
Notes: US EPA Waste Reduction (WAR) Algorithm

## Slide 35: Categories of Environmental Impacts
The WAR Algorithm uses 8 measurable indicators to estimate the environmental impacts of a process.
  Human Toxicity: Ingestion
  Human Toxicity: Dermal/Inhalation
  Aquatic Toxicity
  Terrestrial Toxicity
  Global Warming
  Ozone Depletion
  Photochemical Oxidation
  Acidification
Obviously, we will require data for each chemical entering and leaving our process.
Notes: The key here is that data is required. The EPA maintains a database of chemical species, but many specialty chemical products will be difficult to find. This is a problem with this method.

## Slide 36: PEI Balance Equations
PEI balance for a process and energy generation system:
For a steady-state process, this can be simplified to:
If the waste energy for the process is negligable:
Which can finally be written as:
Notes: The algorithm itself is fairly simple – it is accessing appropriate data than can be problematic.

## Slide 37: Nomenclature
Amount of PEI of the chemical process plus energy generation process, PEI/kg
Input rate of PEI impact to the chemical process, PEI/kg
Output rate of PEI impact to the chemical process, PEI/kg
Input rates of PEI impact to the energy generation process, PEI/kg
Output rate of PEI impact to the energy generation process, PEI/kg
Output of PEI for waste energy lost from the chemical process, PEI/kg
Outputs of PEI for waste energy lost from the energy generation process, PEI/kg
Rate of generation of PEI inside the system, PEI/kg
Notes: Definitions of variables used with the WAR Algorithm.

## Slide 38: Overall PEI Input / Output Balance
Notes: This figure illustrates the basic mass and energy balance for the WAR Algorithm.

## Slide 39: Weighting Factors
The impact estimation algorithm is flexible and allows users to emphasize or deemphasize different impact categories as needed for particular applications.
For example, an operation in an area suffering from smog might emphasize air pollution effects, while an operation where workers are routinely exposed to chemicals might emphasize human health effects.
For an initial assessment, it is often OK to simply weight all impact categories equally.
However, when considering potential carbon legislation, it may be useful to emphasize the GWP category.
Notes: Determining how to weight the factors is important. This will usually depend on the specific environmental conditions or regulatory climate in a given location. For general assessment, keep them set to one – the default value.

## Slide 40: Limitations
It should be noted that there are some important limitations to using the WAR algorithm for an analysis of this type.
Although the WAR algorithm provides an effective means of comparing process options with a similar basis, it cannot evaluate the impacts of switching from a crude oil to a renewable, biomass derived feed stock.
Therefore one should use caution when directly comparing the PEI calculated for sustainable processes with that calculated for processes based on crude oil derived feedstocks.
Notes: In general, the WAR Algorithm is a tool that is best used to evaluate the relative difference between different options or process configurations for the SAME process.

## Slide 41: WAR Graphical User Interface
Notes: Note to Instructor: Students will get practice using the WAR Algorithm during the Inquiry Activities included with this Module.

## Slide 42: Download the WAR GUI
The WAR Algorithm GUI can be downloaded for free from the EPA website.
http://www.epa.gov/nrmrl/std/cppb/war/sim_war.htm
Notes: Note: Some Mac users have reported problems downloading the GUI.

## Slide 43: Main Navigation Screen
Notes: Data can either be added manually or imported directly from Aspen Plus (although I have found the Aspen Interface a bit squirrelly at times).

## Slide 44: Add Chemicals
Notes: The chemicals available in GUI are from the AIChE DIPPR database, so it is fairly extensive.

## Slide 45: Viewing Chemical Data
Notes: We have the option of entering this data manually for a non-database chemical species.

## Slide 46: Energy Contribution
Notes: Since the source of energy effects the PEI, the algorithm allows three choices for energy sources. Obviously utilization of a “Green” energy source would not need to be included.

## Slide 47: Introduction to Life Cycle Assessment Theory
This section contains material adapted from: Allen, D.T. and D.R. Shonnard (2012): “Sustainable Engineering – Concepts, Designs and Case Studies”, Prentice Hall, Upper Saddle River, NJ.
Notes: Life Cycle Assessment differs from Environmental Impact Assessment, in that it considers the entire product life – from raw material extraction from the Earth to energy production to final product disposal In other words, a life cycle for a manufactured product covers the entire scope of the process, from “cradle to grave”.

## Slide 48: So What is a Life Cycle Assessment
The potential environmental impacts of a product extend far beyond the manufacturing process.
We’ve seen a tool that does a good job estimating the impacts, within the battery limits of the plant, but that’s only part of the story.
To truly tell the story, we need to track a product from “cradle to grave”.
In other words, from obtaining raw materials out of the ground to final disposal.
This encompasses every step in the product and manufacturing supply chain.
So What Can a Life Cycle Assessment Tell Us???
Notes: If defining the product life cycle sounds like an enormous task… it is! This is the principle reason we don’t do more life cycle analyses!

## Slide 49: So Why Do Life Cycle Assessment?
Minimize Environmental Impacts
  Minimize the magnitude of pollution
  Conserve non-renewable resources
  Conserve ecological systems
  Develop and utilize cleaner technologies
  Maximize recycling of materials and waste
  Apply the most appropriate pollution prevention technologies
Improve Economic Performance
  Reduce Supply Chain Costs
  Reduce energy expenses
  Improve corporate image to customer/shareholder
Improve Societal Performance
  Become a better steward of natural resources
Notes: As we’ve said before, the one of the goals of sustainability is balance between environment, society and economy.
LCA is a measuring stick for our performance.

## Slide 50: Who Uses Life Cycle Assessment
Manufacturers
  Product development
  Product improvement
  Product comparison
Regulators (potentially)
  Ensure compliance
  Monitor performance
Policy Makers
  Environmental Labeling
Notes: Life cycle assessment has been applied in many ways in both the public and private sectors. This is a list of some of the uses manufacturers have for LCA. Product comparisons have received the most attention from the press but according to the Swedish survey the most important uses for manufacturers are:
to identify processes, ingredients, and systems that are major contributors to environmental impacts,
To compare different options within a particular process with the objective of minimizing environmental impacts, and
To provide guidance in long-term strategic planning concerning trends in product design and materials.
Besides environmental labeling programs, public sector uses of life-cycle methodologies include use as a tool for making procurement decisions and developing regulations. Policymakers report that the most important uses of LCA are in:
helping to develop long-term policy regarding overall material use, resource conservation and reduction of environmental impacts and risks posed by materials and processes throughout the product life-cycle,
evaluating resource effects associated with source reduction and alternative waste management techniques, and
providing information to the public about the resource characteristics of products or materials.

## Slide 51: Simplified Life Cycle Diagram
What data do we need to calculate impacts at each step?
What impacts are we concerned with?
Notes: What you should note here is the inclusion of both transportation and final disposal.

## Slide 52: Steps in a Life Cycle Assessment
Determine the system boundaries and the scope of the assessment.
  A product lifecycle can often be enormous. Consider all the parts and process used in the manufacture of a automobile! We need a way to limit the scope to keep it manageable.
Determine the life cycle inventory.
  This process can be time consuming. The inventory includes inputs like raw materials and energy, and outputs like products, wastes and emissions.
Assess the environmental impacts of the inputs and outputs from the life cycle inventory.
  Impacts can include energy use, pollution, greenhouse gas emission, water use, etc.
Interpret the results.
Notes: For more detail, refer to:
Allen, D.T. and D.R. Shonnard (2012): “Sustainable Engineering – Concepts, Designs and Case Studies”, Prentice Hall, Upper Saddle River, NJ.

## Slide 53: Determining the Functional Unit
This may be the most critical step…
For Example:
  Consider the debate of Paper vs. Plastic grocery bags…
  What is the Function? To carry groceries…
Therefore the functional unit may be volume of groceries carried, not the bag itself.
As we know, different bags have different volumes.
Notes: The functional unit determines equivalence between systems. Choosing a functional unit is not always straightforward and can have a profound impact on the results of the study. For example, if paper and plastic grocery sacks are to be compared in an LCA, the functional unit would be a given volume of groceries. Because fewer groceries, in general, are placed in plastic sacks than in paper sacks, the sacks would not be compared on a 1 to 1 basis. Instead, two plastic sacks might be determined as having the equivalent function of one paper sack.
For more details on the Paper vs. Plastic and other life cycle “debates”, see:
Allen, D.T. and D.R. Shonnard (2012): “Sustainable Engineering – Concepts, Designs and Case Studies”, Prentice Hall, Upper Saddle River, NJ.

## Slide 54: The Life Cycle Inventory
Figure Reference: Allen, D.T. and D.R. Shonnard (2012): “Sustainable Engineering – Concepts, Designs and Case Studies”, Prentice Hall, Upper Saddle River, NJ.
Notes: This looks simple – it’s not! The basics, though, are easy to understand. The life cycle inventory is simply the sum of everything that goes into and out of the process for manufacturing a product. When we tally up all these inputs and outputs for all the raw materials that go into our product, including transportation, and the emissions that are generated from our product, including transportation and use and disposal by the consumer, we have the life cycle inventory. As you can imagine this is an enormous undertaking, and getting the data we need is sometimes a challenge.
This is why it’s important to limit the scope to keep the problem manageable.

## Slide 55: Defining the Environmental Impacts of Interest
Much like the WAR Algorithm, the assessment tools for LCA have to be “tuned” based on the environmental impacts of interest.
Often this is energy, but not always. Some typical factors include:
  Conventional pollutants discharged to the environment, including greenhouse gas emissions.
  Hazardous and toxic waste.
  Energy inputs, including fuels and electricity.
  Resources, such as ores, fertilizer and water
This is a simplification, and additional impact categories can be considered as required.
Notes: As usual, this comes down to our common themes of decision making and engineering judgment.

## Slide 56: Uncertainty in LCA
As with all estimation methods, uncertainty must be considered.
Although we can never eliminate uncertainty, we must be aware of its sources.
Potential sources for uncertainty may include:
  Errors of omission
  Lack of sufficient data
  Reliance on aggregate data
  Supply chain variation
  Standard operating variation
  Changes over time.
Obviously, the more detailed the LCA, the less the uncertainty.
Notes: But at what cost??? This is the primary problem with a detailed LCA. This is a large, costly and time consuming undertaking, especially when uncertainty is taken into account.

## Slide 57: Introduction to Inherently Safe Process Design
Notes: Inherently Safe Design is one of the 12 Principles of Green Chemistry, as described earlier.

## Slide 58: How can we, as Design Engineers, address the inherent hazards of a chemical process?
Page | 58
Notes: We’ll answer this question by taking a look at a design heuristic called Inherently Safe Process Design.
For more information, see:
T. Kletz, Process Plants: A Handbook for Inherently Safety Design, Taylor and Francis, 1998.

## Slide 59: Inherently Safe Process Design
Inherent safety is a concept based on eliminating the causes and/or reducing the consequences of potential process upsets.
Inherently Safe Process Design is a technique applied during the conceptual phase of process design.
Inherently Safe Process Design targets the HAZARD, rather than reducing the RISK after the fact.
This technique is based on making inherently safer design choices at a point in the process development where the engineer has the most influence on the final design.
Page | 59
Notes: It’s important to point out that and inherently safe process does not necessarily pose a lower risk that a “traditional” process. The difference is that a traditional process required additional independent protection layers to mitigate potential process upsets. Both the inherently safe and traditional processes can achieve the same level risk, however, the inherently safe process is simpler and often less expensive than the traditional process. Additionally, upkeep, maintenance and testing requirements are much lower for the inherently safe process.
Students often struggle with understanding the difference between Hazard and Risk. A good example is travel in a commercial jet. This activity is extremely hazardous, because a catastrophic failure at 35,000 feet is not survivable. However, this jet travel is extremely low risk, due to the safeguards used by both the manufacturers and the airlines.

## Slide 60: Inherently Safe Process Design
Inherently safe process design can be grouped into 5 categories
Each of these inherently safer design choices is applied in the conceptual phase of development.
1
Intensification
Continuous reactor vs. batch reactor
2
Substitution
Change of feedstock
3
Attenuation
Alternate technology
4
Limitation of effects
Minimization of storage volume
5
Simplification
Gravity flow vs. pumping
Category
Example
Page | 60
Notes: These are often difficult to implement in existing processes. That’s why it is important to be thinking about inherently safe process design during the conceptual phase of process design. Remember, it is at the earliest stages of design where the process engineer has the greatest influence on the final process performance – from and economic and environmental perspective.
Again, for more information, see:
T. Kletz, Process Plants: A Handbook for Inherently Safety Design, Taylor and Francis, 1998.

## Slide 61: Inherently Safe Process Design – Example
Azeotropic Distillation vs. Pervaporation
Page | 61
Notes: This illustration describes a typical process for breaking a propanol – water azeotrope using hexane as an entrainer. This process is technologically effective, but introduces a large quantity of a flammable material – hexane. In addition, the Azeotrope column is much larger due to the presence of hexane in the system.
For further background on this process, please refer to:
Seay, J.R. and J. Gish (2010): “A Sustainable Design Project for the Process Separations Class”, Center for Sustainable Engineering Electronic Library, Online Publication www.engineeringpathway.com.

## Slide 62: Traditional Process – Sample Risk Assessment
Sample Risk Assessment using What If? Methodology:
Consider what types of safeguards would be required to mitigate the Process Risk due to these scenarios.
Page | 62
Notes: Note that there are many other potential risks. As a students exercise, brainstorm as many additional “what if…?” scenarios as you can.
For further reading on tools for hazard assessment, refer to:
Environmental Protection Agency, Process Hazard Analysis, 40 CFR 68.67, 2005.
Occupational Safety and Health Administration, Process Safety Management of Highly Hazardous Chemicals, 29 CFR 1910.119, 2005.
Center for Chemical Process Safety, Layer of Protection Analysis – Simplified Process Risk Assessment, AIChE, 2001.
Center for Chemical Process Safety, Guidelines for Engineering Design for Process Safety, AIChE, 1993.

## Slide 63: Inherently Safe Process Design – Example
Azeotropic Distillation vs. Pervaporation
Page | 63
Notes: In this process, the entrainer vessel is replaced with a pervaporation unit. This unit utilizes a membrane to move the feed beyond the azeotrope composition. As a result, the hexane is eliminated and the Azeotrope is much smaller.

## Slide 64: Sample Risk Assessment - Inherently Safer Process
When considering the potential upset scenarios for the process, the benefits of the inherently safer process become clear.
Based on this risk comparison, it is clear that multiple independent protection layers would be required to mitigate the operating risk of the traditional process.
This risk can be reduced by designing an inherently safer, ie, less hazardous process.
Although a complete economic analysis would be required, this example has illustrated that the need for independent protection layers is reduced in the inherently safer process design.
Page | 64
Notes: Looking back at a few upset scenarios, the inherently safer process fares better from a safety perspective. Note – this does not mean that the risk is lower! Both the traditional and inherently safer process can achieve the same level of risk. The inherently safer process just requires fewer independent protection layers to mitigate the process hazards. This often means that the inherently safer process is cheaper to operate.
For further reading refer to:
Seay, J. and M. Eden, “Incorporating Risk Assessment and Inherently Safer Design Practices into Chemical Engineering Education”, Journal of Chemical Engineering Education, 2008.

## Slide 65: Module Summary
Green Chemistry is an important consideration in the design of chemical processes.
The 12 principles of Green Chemistry are an important heuristic for chemical process design.
Numerous tools are needed to properly assess the degree to which one process is “greener” or more sustainable than another.
  US EPA Waste Reduction Algorithm
  Life Cycle Assessment
  Inherently Safe Design
Notes: This completes the Green Chemistry educational module. For additional practice and reinforcement, refer to the Inquiry Activity included with this package.

## Slide 66: References and Resources
References
Allen, D.T. and D.R. Shonnard (2012): “Sustainable Engineering – Concepts, Designs and Case Studies”, Prentice Hall, Upper Saddle River, NJ.
Allen, David and David Shonard, (2001). Engineering: Environmentally Conscience Design of Chemical Processes, Prentise-Hall, Upper Saddle River, NJ.
Anastas, P.T. and J.C.Warner, (1998). Green Chemistry: Theory and Practice, Oxford University Press, New York, New York.
Environmental Protection Agency, Process Hazard Analysis, 40 CFR 68.67, 2005.
Occupational Safety and Health Administration, Process Safety Management of Highly Hazardous Chemicals, 29 CFR 1910.119, 2005.
Center for Chemical Process Safety, Layer of Protection Analysis – Simplified Process Risk Assessment, AIChE, 2001.
T. Kletz, Process Plants: A Handbook for Inherently Safety Design, Taylor and Francis, 1998.
Center for Chemical Process Safety, Guidelines for Engineering Design for Process Safety, AIChE, 1993.
Seay, J.R. and J. Gish (2010): “A Sustainable Design Project for the Process Separations Class”, Center for Sustainable Engineering Electronic Library, Online Publication www.engineeringpathway.com.
Seay, J. and M. Eden, “Incorporating Risk Assessment and Inherently Safer Design Practices into Chemical Engineering Education”, Journal of Chemical Engineering Education, 2008.
Young, Douglas, Richard Scharp and Heriberto Cabezas (2000): “The waste reduction (WAR) algorithm: environmental impacts, energy consumption, and engineering economics”, Waste Management, Vol. 20.
On-Line Resources
EPA Green Chemistry
http://www.epa.gov/greenchemistry/

## Slide 67: Acknowledgement
The development of this module has been supported through funding from the US National Science Foundation, award number 1140000, award title: RCN-SEES: Sustainable Manufacturing Advances in Research and Technology (SMART) Coordination Network.