## Slide 1: Life Cycle Assessment (LCA) for Sustainable Manufacturing
Debalina Sengupta
Texas A&M University, College Station, TX

## Slide 2: Overview
Where do we fit?
Why do we need to know about LCA?
What do we need to know about LCA?
How do we conduct an LCA?
Notes: This slide gives an overview of the objectives

## Slide 3: Process Engineering, as we know it!
Corn Stover to Ethanol: HYSYS PROCESS DESIGN
Sengupta, Debalina, and Ralph W. Pike. Chemicals from biomass: integrating bioprocesses into chemical production complexes for sustainable development. CRC Press, 2012.
MACROSCOPIC VIEW FOR PROCESS ENGINEERS:
CORN STOVER TO ETHANOL
(Enzymatic Hydrolysis and Fermentation)
TARGETS:
Maximize yield of ethanol
Maximize profit
Minimize waste
INPUTS
Materials
Water
Energy
OUTPUTS
Product
Co-product
Waste (air, water, soil, other)
Notes: We, chemical engineers are comfortable with (from our undergraduate and some graduate work) process design and engineering. These are examples of what we control, where our expertise lies. This is an example of a corn stover to ethanol process, designed in HYSYS. Corn stover is the primary raw material in this process, which undergoes acid and enzymatic hydrolysis stages of pretreatment to release sugars, followed by fermentation and separation of ethanol from water. This process has several input of raw materials and output of products, along with energy streams. For a process engineer, the details are necessary, but from a macroscopic view, one is able to compute the quantities associated with each flow. The targets a process engineer need to achieve include maximizing profit, yield of ethanol or minimizing waste generation.

## Slide 4: Design Details
Pretreatment of Stover to Release Sugars
  Two step hydrolysis of cellulose and hemicellulose
Fermentation of Sugars to Ethanol
  Yeast/bacterial fermentation of sugars to ethanol
Separation and Purification of Ethanol
  Distillation columns to separate the ethanol from water, followed by membrane separation to retrieve ethanol from the water-ethanol azeotrope

## Slide 5: What follows the design?
Plant design acceptable/profitable
Plant site selected, detailed design, and facility gets built

## Slide 6: What “others” see at the plant

## Slide 7: Where does the stover come from?

## Slide 8: Where does ethanol go to?

## Slide 9: Overall Picture of Corn Stover to Ethanol
Corn Cultivation
Corn Stover Collection
Corn Stover Transport
Ethanol Facility
Ethanol Transport
Ethanol Blending with Gasoline
Fuel Distribution
Fuel End-use in Cars
Where we fit
(Process Engineers)
Ethanol Facility
What we (can theoretically) control
Inputs:
Corn Stover
Water
Energy
Chemicals
Enzymes
Outputs:
Ethanol
Carbon dioxide
Other emissions (VOCs etc.)
Other Wastes
Yields, Recycles, Technology

## Slide 10: LCA gives a “Bigger Picture”
The upstream and downstream effects of a process are often the deciding factors for new technology to the market
  In the case of corn stover, the transportation of stover from the field to the plant gate is expensive because of low density, which makes it an expensive feedstock
  The challenges in yield of sugars from the cellulosic feedstock are yet to be addressed
  The ethanol federal policy subsidizes the blenders
  Mandates are hard to meet as the cost for plant setup and operation is borne by the producers
  Emission profiles for gasoline and ethanol will vary when the two fuels are considered

## Slide 11: Need for LCA for Process Engineers
Process engineering is at the “heart” of commercialization of a new technology
New technology needs the macroscopic view to make it “truly” viable
  Biomass use is GOOD – general consensus, as carbon dioxide released from biomass can be fixed easily over shorter time than fossil fuels
  BUT - Water use, energy use, volatile emissions is higher compared to gasoline
  Maybe using biomass is not so “green” after all!
Insights from LCA can be used for targeting the hotspots within a process
  Identification of emissions with respect to the rest of the life cycle can trigger the installation of better control equipment at the facility level
  Governmental policies for facilities can be set based on the results of LCA
  Comparison to other competing fuels can be made
With this background,
we will learn about the methods of LCA
perform a hands on training on how to do an LCA

## Slide 12: Life Cycle Assessment - Definition
The International Organisation for Standardisation (ISO) defines LCA as:
  A compilation and evaluation of the inputs, outputs and potential environmental impacts of a product throughout its lifecycle
Industrial Ecology defines LCA as:
  The life cycle assessment is an objective process to evaluate the environmental burdens associated with a product, process or activity by identifying, quantifying and assessing the impact of energy and material usage and environmental releases and to implement opportunities to effect environmental considerations
In essence:
  Life Cycle Assessment (LCA) is a technique used to quantify the environmental impact of a product from raw material acquisition through end of life disposition (cradle-to-grave)
Message:
Quantify Inputs, Outputs, Environmental impacts/burdens
Follow a product’s full life cycle to make a definitive decision
Systematic procedure required for managing the vast information

## Slide 13: Generic Product Life Cycle
Material Acquisition
Material Processing
Manufacture and Assembly
Use and Service
Retirement and Recovery
Treatment or Disposal
Inputs:
Materials
Energy
Water
Air
Outputs:
Principal Products
Co-products
Water effluents
Air emissions
Solid waste
Other Environmental Effects

## Slide 14: Life Cycle Assessment Methodology
The LCA methodology is standardised by a series of ISO standards
  Step 1: Goal and scope definition
    Identify the LCA's purpose, the products of the study, and determine the boundaries. (what is and is not included in the study)
  Step 2: Inventory Analysis (LCI)
    Quantify the energy and raw material inputs and environmental releases associated with each life cycle phase
  Step 3: Impact Assessment (LCIA)
    Assess the impacts on human health and the environment.
  Step 4: Interpretation
    Evaluate opportunities to reduce energy, material inputs, or environmental impacts at each stage of the product life-cycle.

## Slide 15: Step 1: Goal and scope definition
Define the goal:
  Intended application of the study
  Intended audience
Define the scope:
  Identify the product system to be studied
  Define the functional unit
  Define the boundaries of the product system
  Identify assumptions and limitations of the study
  Select impact categories to be included

## Slide 16: Step 2: Inventory Analysis (LCI)
Possibly the most important step for process engineers
Highly data intensive
Detailed mass & energy balances performed over life-cycle
Advantages: measure data & define baseline metrics of life-cycle processes
Challenges: Assumptions made when data unavailable

## Slide 17: Life Cycle Assessment Tools and Databases
 | Open-LCA | SimaPro | GaBi
User base | Mixed but small | Academia | Academia, Industry, DOE
Visualization | Process-based – flexible | Result-based | Process-based/Result-based
Technical support | Least capacity | Good | Excellent, but expensive
Modelling issues | Highly flexible | Limited treatment of recycling loops | More advanced treatment of recycling loops
 | Ecoinvent | GaBi
No. of unit processes | ~4500 | 4000+
Scope issues | Better coverage of infrastructure and transport inputs | 
Aggregation of data | Very little (plastics) | Highly
Sources | Mixed; most from statistical abstracts; some from industry | More direct from industry
US coverage | Limited | Better with US edition
Documentation | Public; all unit process data published; sources published; authors with contact info included | Public metadata and process model; hide inputs and outputs; calculation assumptions not published
Uncertainty | For all inputs based on transparent but semi-quantitative procedure | Not always quantified
Format | Ecospold 1.2 | ILCD, 1.1
Last update | V2.2, 2010 | 2006 (smaller updates with software)
Databases:
Tools:

## Slide 18: Step 3: Impact Assessment (LCIA)
Converts the inventory into impact categories or mid/end points which explain the environmental effect
Impact categories may include: carcinogens, respiratory organics and inorganics, climate change, radiation, ozone layer, ecotoxicity, acidification/eutrophication, land use, minerals, fossil fuels
Advantages: grouping of several different pollutants into a single effect for easy interpretation
Challenges: Not all pollutant effects are well known or characterized

## Slide 19: Life Cycle Impact Assessment (LCIA)
The Life Cycle Impact Assessment (LCIA) phase of an LCA is the evaluation of potential human health and environmental impacts of the environmental resources and releases identified during the LCI. Impact assessment should address ecological and human health effects; it should also address resource depletion. A life cycle impact assessment attempts to establish a linkage between the product or process and its potential environmental impacts.
Life Cycle Impact Assessment is computation of potential impacts rather than real.
Midpoint versus Endpoint – Midpoint reporting minimizes the amount of forecasting and effect modeling incorporated into the LCIA
Results of an LCIA show the relative differences in potential environmental impacts

## Slide 20: Life Cycle Impact Assessment (LCIA)
Selection and Definition of Impact Categories - identifying relevant environmental impact categories (e.g., global warming, acidification, terrestrial toxicity).
Classification - assigning LCI results to the impact categories (e.g., classifying carbon dioxide emissions to global warming).
Characterization - modeling LCI impacts within impact categories using science-based conversion factors (e.g., modeling the potential impact of carbon dioxide and methane on global warming).
Normalization - expressing potential impacts in ways that can be compared (e.g. comparing the global warming impact of carbon dioxide and methane for the two options).
Grouping - sorting or ranking the indicators (e.g. sorting the indicators by location: local, regional, and global).
Weighting - emphasizing the most important potential impacts.
Evaluating and Reporting LCIA Results - gaining a better understanding of the reliability of the LCIA results.

## Slide 21: LCIA Methods
CML 2011 – version Dec 2007, Nov 2009, Nov 2010
CML 1996
Eco-Indicator 95
Eco-Indicator 95 RF
Eco-Indicator 99
EDIP 1997
EDIP 2003
Impact 2002+
Method of Ecological Scarcity (UBP Method)
ReCiPe
TRACI 2.0
USEtox

## Slide 22: Step 4: Interpretation
Life cycle interpretation: Results of inventory analysis and/or impact assessment are evaluated in relation to the goal and scope of the study to reach conclusions and recommendations
Identify significant issues, e.g. whether a process will be viable or not when considered on a life cycle basis
Evaluate results for completeness, consistency, and sensitivity of the data
Draw conclusions and make recommendations consistent with the goal & scope of the study

## Slide 23: LCA Terminology
System Boundary - set of criteria specifying which unit processes are part of a product system
Unit Process - smallest element considered in the life cycle inventory analysis for which input and output data are quantified
Reference Flow - measure of the outputs from unit processes in a given product system required to fulfil the function expressed by the functional unit
Functional Unit - quantified performance of a product system for use as a reference unit
For complete list of terms and definitions, refer to “ISO 14040 - Environmental management — Life cycle assessment — Principles and framework”

## Slide 24: System Boundary - set of criteria specifying which unit processes are part of a product system
From Thermodynamics, we know the concept of System and Surroundings
In LCA, a similar concept is used to determine which units will be considered for the system of study. In the example below, we may consider the life cycle stages from Manufacturing to retirement and recovery, or may choose to omit the material acquisition phase depending on prior knowledge of its impacts.
Material Acquisition
Material Processing
Manufacture and Assembly
Use and Service
Retirement and Recovery
Treatment or Disposal
Material Acquisition
Material Processing
Manufacture and Assembly
Use and Service
Retirement and Recovery
Treatment or Disposal
Material Acquisition
Material Processing
Manufacture and Assembly
Use and Service
Retirement and Recovery
Treatment or Disposal

## Slide 25: Unit Process - smallest element considered in the life cycle inventory analysis for which input and output data are quantified
Unit operations in Chemical Engineering
Process flow diagram denoting the system
Manufacture and Assembly
Use and Service
Retirement and Recovery
Treatment or Disposal
Material Processing
Material Acquisition
System Boundary
Unit Processes
For Life Cycle Assessment, the following is analogous to the process system
Notes: In this slide, an analogy is drawn between Unit Operations within a process plant and Unit Processes in LCA. The process plant boundary can be considered similar to the system boundary.

## Slide 26: Reference Flow - measure of the outputs from unit processes in a given product system required to fulfil the function expressed by the functional unit
Material Acquisition
Material Processing
Manufacture and Assembly
Use and Service
Retirement and Recovery
Treatment or Disposal
Reference Flows connect information from one unit process to another
Typically based on the primary product from a particular unit process
Corn Cultivation
Corn Stover Collection
Corn Stover Transport
Ethanol Facility
Ethanol Transport
Ethanol Blending
Fuel Distribution
Fuel End-use in Cars
Examples:
  1 kg corn stover at field
  1 kg corn stover on truck
  1 km traveled by stover truck
  1 kg ethanol at production facility
  1 kg ethanol on train car
  1 kg blended fuel at gas station

## Slide 27: Functional Unit - quantified performance of a product system for use as a reference unit
Material Acquisition
Material Processing
Manufacture and Assembly
Use and Service
Retirement and Recovery
Treatment or Disposal
Corn Cultivation
Corn Stover Collection
Corn Stover Transport
Ethanol Facility
Ethanol Transport
Ethanol Blending
Fuel Distribution
Fuel End-use in Cars
The unit that defines the function of a system that we are interested in studying
Typically based on the goal of study
Example:
1 kg fuel burnt in passenger car

## Slide 28: Recap of LCA
Systematic accounting of inputs, outputs, and environmental impacts associated with a product from a system
Goal and Scope, Life Cycle Inventory, Life Cycle Impact Assessment, Interpretation of results are the steps of LCA
Definition of system boundary, unit processes, reference flows and functional unit
LCA for process engineers is important :
  Understand the big picture
  Derive insights for process improvement
  Determine/verify mass and energy targets
  Incorporate Life Cycle Thinking or Life Cycle Perspectives in sustainable design of processes. This is more important than the “Assessment” itself.

## Slide 29: Life Cycle Assessment (LCA) Case Study Comparing methanol production routes from carbon dioxide

## Slide 30: Case Study Objectives
Hands-on training on how to conduct an LCA
Basic understanding of system boundary, functional unit, reference flows
Knowledge of LCA tools and databases (Excel® used in case study)
Knowledge of Impact Assessment Methods (case study uses TRACI from US EPA)
Familiarity to compiling a Life Cycle Inventory
Familiarity to conducting Life Cycle Impact Assessment
Results Interpretation

## Slide 31: Problem Definition
Methanol is traditionally produced from natural gas via steam reforming of methane. Methanol can also be produced via catalytic hydrogenation of carbon dioxide. Carbon dioxide is a greenhouse gas and its consumption promises a sustainable option compared to fossil fuel based natural gas feedstock.
This problem will compare the various processes for the production of methanol using life cycle assessment methodology, and determine which process is the best for the production of methanol.

## Slide 32: Goal and Scope
Feedstock Extraction
Methanol Production
Methanol Use
Disposal
Goal: To determine whether a new methanol process which utilizes carbon dioxide as a raw material is better than existing methanol process from steam reforming of natural gas.
Scope: The complete life cycle for methanol production needs to study the feedstock extraction, methanol production, methanol use and final disposal.
For comparing the production routes for methanol, the changes are anticipated only in the methanol production phase.
For this reason, a gate to gate analysis of the methanol production life cycle phase will be sufficient to make a judgment on the acceptability of the process. Thus, we consider the system boundary to include the conventional methanol production, and the methanol production from carbon dioxide.

## Slide 33: Process Description – Conventional Process
Synthesis Gas Preparation
  CH4 + H2O = CO + 3H2 (1)
  The reaction is very endothermic, favored by high temperature and low pressure. This reaction produces 1:3 ratio of CO to H2 instead of the 1:2 needed for methanol synthesis.
  Water-gas shift reaction produces CO.
  CO2 + H2 = CO + H2O (2)
  From Equation (1) and (2), we get:
  3CH4 + 2H2O + CO2 = 4CO + 8H2 (3)
  Methanol Synthesis in Catalytic Converter
  Methanol synthesis occurs in a converter using Lurgi technology
  CO + 2H2 = CH3OH (4)
Notes: Prepare the groups in this session

## Slide 34: Process Description - New Processes
Methanol from CO2 Hydrogenation over Cu(100) Catalyst (Nerlov and Chorkendorff, 1999)
CO2 + 3H2 → CH3OH + H2O ΔHo = -49 kJ/mol, ΔGo = 3 kJ/mol
Methanol from CO2 Hydrogenation over Cu - Zr Catalyst (Toyir et al., 1998)
CO2 + 3 H2 → CH3OH + H2O ΔHo = -49 kJ/mol, ΔGo = 3 kJ/mol
CO2 + H2 → CO + H2O ΔHo = 41 kJ/mol, ΔGo = 29 kJ/mol
Methanol from CO2 Hydrogenation over Cu/ZnO/ZrO2/Al2O3/Ga2O3 Catalyst (Ushikoshi et al., 1998)
CO2 + 3 H2 → CH3OH + H2O ΔHo = -49 kJ/mol, ΔGo = 3 kJ/mol
CO2 + H2 → CO + H2O ΔHo = 41 kJ/mol, ΔGo = 29 kJ/mol
CO + 2H2 → CH3OH ΔHo = -90.5 kJ/mol, ΔGo = -25 kJ/mol
Methanol from Hydrogenation over Cu/ZnO/Cr2O3 and CuNaY Zeolite Catalyst (Jun et al., 1998)
CO2 + H2 → CO + H2O ΔHo = 41 kJ/mol, ΔGo = 29 kJ/mol
CO + 2H2 → CH3OH ΔHo = -90.5 kJ/mol, ΔGo = -25 kJ/mol
2CH3OH → CH3OCH3 + H2O ΔHo = -24 kJ/mol, ΔGo = -17 kJ/mol
Methanol from Hydrogenation over Pd/SiO2 Catalyst (Bonivardi et al., 1998)
CO2 + H2 → CO + H2O ΔHo = 41 kJ/mol, ΔGo = 29 kJ/mol
CO + 2H2 → CH3OH ΔHo = -90.5 kJ/mol, ΔGo = -25 kJ/mol
Notes: Prepare the groups in this session

## Slide 35: Streams for various methanol production processes
Inventory of inputs, outputs and energy required for the processes
Process | Input Streams | Flow Rate (Kg/hr) | Output Streams | Flow Rate (Kg/hr)
Nerlov and Chokendorff, 1999 | Carbon Dioxide | 75,540 | Methanol | 54,760
 | Hydrogen | 10,380 |  | 
 | Cooling Water | 18,160,000 |  | 
 | HP Steam | 776,000 |  | 
Toyir et al., 1998 | Carbon Dioxide | 151,400 | Methanol | 54,870
 | Hydrogen | 13,870 | Carbon Monoxide | 48,180
 | Cooling Water | 26,740,000 |  | 
 | HP Steam | 1,205,000 |  | 
Ushikoshi, 2002 | Carbon Dioxide | 76,450 | Methanol | 54,730
 | Hydrogen | 10,420 | Carbon Monoxide | 585
 | Cooling Water | 16,510,000 |  | 
 | HP Steam | 693,000 |  | 
Jun, et al., 1998 | Carbon Dioxide | 79,740 | Methanol | 54,700
 | Hydrogen | 10,940 | Dimethyl Ether (DME) | 2,102
 | Cooling Water | 148,000,000 |  | 
 | HP Steam | 602,000 |  | 
Bonivardi, et al., 1998 | Carbon Dioxide | 79,590 | Methanol | 54,800
 | Hydrogen | 10,570 | Carbon Monoxide | 2,527
 | Cooling Water | 13,180,000 |  | 
 | HP Steam | 525,000 |  | 
Conventional Process | Carbon Dioxide | 7,177 | Methanol | 20,698
 | Methane | 7,782 | Carbon Monoxide | 13.57
 | Cooling Water | 2,498,850 | Carbon Dioxide | 71.76
 | LP Steam | 5,828 | Hydrogen | 2.97

## Slide 36: Environmental Impact Assessment
Tool for the Reduction and Assessment of Chemical and Other Environmental Impacts (TRACI)
http://www.epa.gov/nrmrl/std/traci/traci.html

## Slide 37: Life Cycle Impact Assessment
The life cycle impacts in the following categories can be calculated from the inventory
  Energy Intensity
  Water Intensity
  Material Intensity
  Global Warming Potential
  Smog Formation Potential
  Human Health Impacts Particulate Matter

## Slide 38
Notes: The items in red and green correspond to compounds which have an environmental impact. Carbon dioxide is color coded as green since it is being consumed in the process and has a positive impact. The rest are being released from the process, including methanol, which causes a negative environmental impact. The Cooling Water corresponds to water consumption category. The steam consumption corresponds to energy use category. The energy content of steam is used to compute the energy use in KJ. The material required in the processes are used for the material consumption indicator.

## Slide 39: TRACI Characterization Factors for Impact Categories
Compound | Global Warming Air (kg CO2 eq / kg substance) | HH Particulate Air (PM2.5 eq / kg substance) | Smog Air (kg O3 eq / kg substance)
Carbon Dioxide | 1 | - | -
Methane | 25 |  | 
Carbon Monoxide | - | 3.56E-04 | 5.56E-02
Methanol | - | - | 6.72E-01
I = Impact (or Potential Impact)
Cfi = Characterization Factor of ith species
Ei = Elementary Flow, ith species in Life Cycle Inventory

## Slide 40: Life Cycle Impact Assessment
 | Global Warming Air (kg CO2 eq / kg methanol) | HH Particulate Air (PM2.5 eq / kg methanol) | Smog Air (kg O3 eq / kg methanol) | Energy Intensity (kJ/kg methanol) | Water Intensity (kg/kg methanol) | Material Intensity (kg/kg methanol)
Nerlov and Chokendorff, 1999 | -1.38E+00 | 0.00E+00 | 6.72E-01 | 2.41E+04 | 3.32E+02 | 1.57E+00
Toyir et al., 1998 | -2.76E+00 | 3.13E-04 | 7.21E-01 | 3.74E+04 | 4.87E+02 | 3.01E+00
Ushikoshi et al., 1998 | -1.40E+00 | 3.81E-06 | 6.73E-01 | 2.16E+04 | 3.02E+02 | 1.59E+00
Jun, et al., 1998 | -1.46E+00 | 0.00E+00 | 6.72E-01 | 1.87E+04 | 2.71E+03 | 1.66E+00
Bonivardi, et al., 1998 | -1.45E+00 | 1.64E-05 | 6.75E-01 | 1.63E+04 | 2.41E+02 | 1.65E+00
Conventional | -9.74E+00 | 2.33E-07 | 6.72E-01 | 1.01E+04 | 1.21E+02 | 7.23E-01

## Slide 41: Interpretation of Results Material Intensity
Chart: 
| Nerlov and Chokendorff, 1999 | Toyir et al., 1998 | Ushikoshi et al., 1998 | Jun, et al., 1998 | Bonivardi, et al., 1998 | Conventional
Material Intensity (kg/kg methanol) | 1.569 | 3.012 | 1.5872 | 1.6578 | 1.6453 | 0.72273

## Slide 42: Interpretation of Results Water Intensity
Chart: 
| Nerlov and Chokendorff, 1999 | Toyir et al., 1998 | Ushikoshi et al., 1998 | Jun, et al., 1998 | Bonivardi, et al., 1998 | Conventional
Water Intensity (kg/kg methanol) | 331.6289 | 487.3337 | 301.6627 | 2705.6673 | 240.5109 | 120.7291

## Slide 43: Interpretation of Results Energy Intensity
Chart: 
| Nerlov and Chokendorff, 1999 | Toyir et al., 1998 | Ushikoshi et al., 1998 | Jun, et al., 1998 | Bonivardi, et al., 1998 | Conventional
Energy Intensity (kJ/kg methanol) | 24134.5069 | 37401.7769 | 21564.9242 | 18743.4406 | 16316.1953 | 10141.2387

## Slide 44: Interpretation of Results Global Warming Potential
Chart: 
| Nerlov and Chokendorff, 1999 | Toyir et al., 1998 | Ushikoshi et al., 1998 | Jun, et al., 1998 | Bonivardi, et al., 1998 | Conventional
Global Warming Air (kg CO2 eq / kg methanol) | -1.3795 | -2.7592 | -1.3969 | -1.4578 | -1.4524 | -9.7427

## Slide 45: Interpretation of Results Human Health Impact (Particulate Matter)
Chart: 
| Nerlov and Chokendorff, 1999 | Toyir et al., 1998 | Ushikoshi et al., 1998 | Jun, et al., 1998 | Bonivardi, et al., 1998 | Conventional
HH Particulate Air (PM2.5 eq / kg methanol) | 0 | 0.00031259 | 3.8052e-06 | 0 | 1.6416e-05 | 2.334e-07

## Slide 46: Interpretation of Results Smog Formation Potential
Chart: 
| Nerlov and Chokendorff, 1999 | Toyir et al., 1998 | Ushikoshi et al., 1998 | Jun, et al., 1998 | Bonivardi, et al., 1998 | Conventional
Smog Air (kg O3 eq / kg methanol) | 0.672 | 0.72082 | 0.67259 | 0.672 | 0.67456 | 0.67204

## Slide 47: Results Interpretation - Summary
Based on the results, the conventional process is best in all the categories on a relative scale.
It will be beneficial to keep the conventional process.
Improvement of the other processes based on these results is desired to make them acceptable.

## Slide 48: Acknowledgement
The development of this module has been supported through funding from the US National Science Foundation, award number 1140000, award title: RCN-SEES: Sustainable Manufacturing Advances in Research and Technology (SMART) Coordination Network.