## Slide 1: Industrial Sector Level Management: Pollutant Trading using multi-criteria optimization and decision making under uncertainty

## Slide 2: Problem Statement
Total Maximum Daily Load (TMDL) of 32.8 kilograms/year for mercury for the Savannah River basin
Water quality standard (WQS) of 2.8 ng/l (parts per trillion)
29 major industries (point sources) must comply
Three mercury control technologies available for implementation: Differ in cost and efficiency

## Slide 3: What is Pollutant Trading?
Market based approach to achieve environmental goals at reduced overall costs
Based on the fact that different industries face different costs of control of the same pollutants

## Slide 4: What is Pollutant Trading?
Industry A
Industry B
Money
Pollution Reduction
(Buyer)
(Seller)
Trading allows industries with high control costs to achieve the targets by purchasing equivalent (or higher) pollution reductions from industries with lower control costs

## Slide 5: Pollutant Trading: Industry Perspective
Goal: To reduce cost of compliance
Decisions:
  Waste treatment technology selection
  Decision to trade or not
  Choice of trading partner
  Amount of pollutant to trade
  Availability of capital

## Slide 6: Important system level questions
Will mercury trading reduce the total cost of compliance?
What effect with trading have on the overall health care cost?
How do more accurate nonlinear technology cost models affect the results?
What is the impact of uncertainty in cost models on the results?
How do results change with changing TMDL values and health care cost importance?

## Slide 7: Steps in optimization problem formulation
Identify and list the model parameters for which data are given
Identify the decision variables in the model
Formulate the model constraints
Formulate the economic objective function (cost minimization)
Calculation of the health care cost due to exposure to mercury

## Slide 8: Parameters for point sources
Set of point sources (PSi), i = 1,…,N
Di = Discharge quantity of polluted water from PSi [volume/year]
ci = Current pollutant concentration in discharge water from PSi [mass/volume]
redi = Desired pollutant quantity reduction in discharge of PSi [mass/year]
Pi = Treatment cost incurred by PSi to reduce pollution when trading is not possible

## Slide 9: Parameters mercury control technologies
Set of waste reduction technologies: j = 1,…,M
fj(ϕj, Di) = Cost function for total plant cost for technology j [$]
qj = Pollution reduction possible from the implementation of technology j [mass/volume]
ϕj is the set of design parameters of technology j.

## Slide 10: Parameters for trading implementation
Trading ratio: Units of pollutant reduction a source must purchase to receive credit for one unit of load reduction
Transaction fee: Expenses for trading participants that occur only as a result of trading

## Slide 11: Decision variables
bij: Binary variable representing point source-technology correlation. The variable is 1 when PS i installs technology j, and 0 otherwise.
tik (mass/year): Amount of pollutant traded by PS i with PS k, i.e. PS i pays PS k to take care of its own pollution.

## Slide 12: Constraints

## Slide 13: Objective function
Why is transaction cost not being considered in the objective function?
For linear cost models of mercury control technologies:

## Slide 14: Health care cost calculation

## Slide 15: Health care cost calculation parameters
LC50: Lethal Concentration 50% for mercury
Safe mercury concentration in fishes
: Actual water quality standard
: Final reduction achieved by point source i
: Average fish consumption per person per day
: Average water consumption per person per day
P: Population in the watershed affected
: Health care compensation per mortality

## Slide 16: Programming in GAMS
Declaration of sets and parameter values for model formulation

## Slide 17: Programming in GAMS
Declaration of data table for 29 point source industries

## Slide 18: Programming in GAMS
Declaration of equations, model and solve statement

## Slide 19: Programming in GAMS
Post optimization calculation of health care cost for the model simulation result

## Slide 20: Model modification: Inclusion of health care cost as objective
Health care cost calculation equations are now part of the constraints

## Slide 21: Model Extensions
Model assumptions for mercury control technologies:
  Cost scales linearly with volume (TCj)
  Cost is deterministically known
Both assumptions often violated in reality
  Nonlinear cost functions
  Uncertain technology performance (e.g. conversion, reactant life etc.)
New technologies: Insufficient data leading to uncertainty

## Slide 22: Nonlinear Trading Model
Constraint 1:
Constraint 2:
Annual Cost of Technology j
Objective:
Mixed Integer Nonlinear Programming Problem
Nonlinear technology cost models:

## Slide 23: Nonlinear Stochastic Trading Model
Constraint 1:
Constraint 2:
Objective:
Mixed Integer Stochastic Nonlinear Programming Problem
Nonlinear technology cost models:

## Slide 24: Trading Model: Two Stage Formulation
MISNLP problems are computationally difficult to solve
Formulation of a two stage problem:
  Combination of successive MIP and LP problem
Constraints:
Objective:
First stage problem: Uses a linear approximation of nonlinear cost models
Technology selection (binary) and trading (continuous) decisions

## Slide 25: Trading Model: Two Stage Formulation
Use of L-shaped method for problem solution
  Established method for the solution of two or multiple stage stochastic programming problems
Second stage problem: Computes the exact costs using nonlinear cost models and multiple samples
Constraints:
Objective:
Nsamp: Sample size used to sample the uncertain parameters