## Slide 1: Green Engineering: Application of Metrics and the Presidential Green Chemistry Challenge Award
Level 1 Metrics Case Studies
Ibuprofen
Maleic Anhydride

## Slide 2: GC Metrics - Ibuprofen Example
Ibuprofen is an over the counter pharmaceutical nonsteroidal anti-inflammatory drug (NSAID) with 35 million pounds/year produced.
In the 1960’s, the Boots Company patented a synthesis of Ibuprofen (scheme 1)
A 6 step process with large quantities of waste and unwanted byproducts
In 1991, BHC Company patented a 3 step process with increased atom economy and decreased unwanted products.
Awarded the 1997 Presidential Green Chemistry Challenge Award for Greener Synthetic Pathways
Implemented by now BASF in Bishop TX producing 35 million pounds/year

## Slide 3: GC Metrics - Ibuprofen Scheme 1
6 steps
= 40%
Significant amounts of aqueous salt solution waste
No Catalysis
The BHC Company Synthesis of Ibuprofen. From Cann MC, Connelly ME. Real World Cases in Green Chemistry. American Chemical Society, Washington, DC, 2000.

## Slide 4: GC Metrics - Ibuprofen Scheme 2
3 steps
= 77%
AE is > 99% if the acetic acid is recovered from step 1 as a product.
“The anhydrous hydrogen fluoride catalyst/solvent is recovered and recycled with greater than 99.9 percent efficiency. No other solvent is needed in the process, simplifying product recovery and minimizing fugitive emissions.” EPA PGCCA

## Slide 5: GC Metrics - Ibuprofen Example
Conclusions
By incorporating a catalyst, a 6 step process goes to 3 steps with greater Atom Economy from 40% to 77%.
Generally, each step involves a reaction followed by a separation; each of which has waste, requires materials and energy, etc.
Analysis can be expanded to include yields, workup materials, energy efficiency, toxicity analysis …

## Slide 6: GC Metrics – Maleic Anhydride Example
World production of Maleic Anhydride is 1.5 million tons per year.
Primarily used in the manufacture of polyester resins for construction, automotive and marine applications
Other applications are in chemicals, agriculture, consumer products, food, and personal care products industries
Two primary oxidative reaction pathways are used to produce MA.
Benzene route
n-butane route

## Slide 7: Benzene route to Maleic Anhydride
Controlled benzene oxidation is the traditional method.
+ 9/2 O2
V2O5
MoO3
+ 2 H2O + 2 CO2
 | Benzene | Oxygen | Maleic Anhydride | Water | Carbon Dioxide
MW (g/mol) | 78.1 | 32.0 | 98.1 | 18.0 | 44.0
Stoichiometric Mass Ratio | 0.80 | 1.47 | 1.0 | 0.37 | 0.90
TLV (ppm) | 0.5 | - | 0.25 | - | 5000
PEL (ppm) | 1-5 | - | 0.25 | - | 
REL (ppm) | 0.1 | - | 0.25 | - | 

## Slide 8: Benzene route to Maleic Anhydride
Controlled benzene oxidation is the traditional method.
*byproducts not accounted for.
+ 9/2 O2
V2O5
MoO3
+ 2 H2O + 2 CO2

## Slide 9: Benzene to MA side reactions
To avoid quinone production, Run with excess O2 at 13.5:1 O2:C6H6 ratio
Result is lower MA yield due to CO2 formation
C6H6 + 3/2 O2  C6H4O2 + 2 H2O
benzene quinone
C6H6 + 15/2 O2  6 CO2 + 3 H2O
C4H2O3 + 3 O2  4 CO2 + H2O
MA

## Slide 10: n-butane to MA
C4H10 + 7/2 O2
(VO)2P2O5
+ 4 H2O
Controlled n-butane oxidation is the new method.
 | n-butane | Oxygen | Maleic Anhydride | Water
MW (g/mol) | 58.1 | 32.0 | 98.1 | 18.0
Stoichiometric Mass Ratio | 0.59 | 1.14 | 1.0 | 0.73
TLV (ppm) | 1000 | - | 0.25 | -
PEL (ppm) | 800 | - | 0.25 | -
REL (ppm) | 800 | - | 0.25 | -

## Slide 11: n-butane to MA
C4H10 + 7/2 O2
(VO)2P2O5
+ 4 H2O
Controlled n-butane oxidation is the new method.

## Slide 12: n-butane to MA side reactions
Assume:
MA Selectivity = 55%
n-butane conversion = 85%
SF = 1 and MRP = 1
Yield = 46.8%
C4H10 + (5+4x)/2 O2  4 COx + 5 H2O
C4H2O3 + (2x-1) O2  4 COx + H2O
MA

## Slide 13: Benzene to MA PFD
1
4
Reactants
13
7
12
Conversion
Waste
Product
R.Turton, .C.Bailie, W.B.Whiting, and J.A.Shaeiwitz; Analysis, Synthesis and Design of Chemical Processes, 3/E ; Prentice Hall

## Slide 14: PFD Molar Flowrates
Stream No. | 1 | 4 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Temperature (°C) | 30 | 30 | 460 | 608 | 260 | 329 | 320 | 194 | 84 | 189 | 329
Pressure (kPa) | 101 | 101 | 235 | 220 | 215 | 80 | 100 | 82 | 75 | 70 | 80
Total (kmol/h) | 42.3 | 2790 | 2832.3 | 2825.2 | 2825.3 | 500.1 | 0.1 | 526.2 | 2797.9 | 26.2 | 500
Total (kg/h) | 3304 | 80490 | 83794 | 83794 | 83794 | 139191.6 | 30.6 | 141866 | 81225 | 2597 | 139269
Flowrates (kmol/h) |  |  |  |  |  |  |  |  |  |  | 
Maleic Anhydride | - | - | 0 | 26.3 | 26.3 | - | - | 24.8 | 0.5 | 24.8 | -
Dibutyl Phthalate | - | - | 0 | - | - | 500.5 | 0.1 | 500.4 | 0.1 | - | 500.4
Nitrogen | - | 2205 | 2205 | 2205 | 2205 | - | - | - | 2205 | - | -
Water | - | - | 0 | 91.5 | 91.5 | - | - | - | 90.5 | - | -
Oxygen | - | 585 | 585 | 370.2 | 370.2 | - | - | - | 370.2 | - | -
Benzene | 42.3 | - | 42.3 | 2.6 | 2.6 | - | - | - | 2.6 | - | -
Quinone | - | - | - | 0.7 | 0.7 | - | - | 0.4 | 0.4 | 0.4 | -
Carbon Dioxide | - | - | 0 | 129 | 129 | - | - | - | 129 | - | -
Maleic Acid | - | - | 0 | - | - | - | - | 1 | - | 1 | -
R.Turton, .C.Bailie, W.B.Whiting, and J.A.Shaeiwitz; Analysis, Synthesis and Design of Chemical Processes, 3/E ; Prentice Hall

## Slide 15: Benzene to MA PFD Flowrates
Stream No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Temp (°C) | 30 | 30 | 30 | 30 | 145 | 460 | 608 | 260 | 329 | 320 | 194 | 84 | 189 | 329 | 419 | 561
Pres (kPa) | 101 | 101 | 280 | 101 | 250 | 235 | 220 | 215 | 80 | 100 | 82 | 75 | 70 | 80 | 200 | 200
Total (kmol/h) | 42.3 | 42.3 | 42.3 | 2790 | 2790 | 2832.3 | 2825.2 | 2825.3 | 500.1 | 0.1 | 526.2 | 2797.9 | 26.2 | 500 | 5000 | 5000
Total (kg/h) | 3304 | 3304 | 3304 | 80490 | 80490 | 83794 | 83794 | 83794 | 139191.6 | 30.6 | 141866 | 81225 | 2597 | 139269 | 391925 | 391925
Flowrates (kmol/h) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Maleic Anhydride |  |  |  |  |  | 0 | 26.3 | 26.3 |  |  | 24.8 | 0.5 | 24.8 |  |  | 
Dibutyl Phthalate |  |  |  |  |  | 0 |  |  | 500.5 | 0.1 | 500.4 | 0.1 |  | 500.4 |  | 
Nitrogen |  |  |  | 2205 | 2205 | 2205 | 2205 | 2205 |  |  |  | 2205 |  |  |  | 
Water |  |  |  |  |  | 0 | 91.5 | 91.5 |  |  |  | 90.5 |  |  |  | 
Oxygen |  |  |  | 585 | 585 | 585 | 370.2 | 370.2 |  |  |  | 370.2 |  |  |  | 
Benzene | 42.3 | 42.3 | 42.3 |  |  | 42.3 | 2.6 | 2.6 |  |  |  | 2.6 |  |  |  | 
Quinone |  |  |  |  |  |  | 0.7 | 0.7 |  |  | 0.4 | 0.4 | 0.4 |  |  | 
Carbon Dioxide |  |  |  |  |  | 0 | 129 | 129 |  |  |  | 129 |  |  |  | 
Maleic Acid |  |  |  |  |  | 0 |  |  |  |  | 1 |  | 1 |  |  | 
Sodium Nitrite |  |  |  |  |  | 0 |  |  |  |  |  |  |  |  | 2065.6 | 2065.6
Sodium Nitrate |  |  |  |  |  | 0 |  |  |  |  |  |  |  |  | 2934.4 | 2934.4

## Slide 16: Metrics from PFD for Benzene Process
31.3 (includes N2 inert)
Yield: R-601 Yield = 0.62 Overall Yield=
12
13

## Slide 17: n-butane to MA PFD
1
2
8
7
11
5
12
13
15
14
9
R-101 Reactor to Produce MA
T-101 Separate Light Gases
V-101 Purification, MA converted to Maleic acid
R-102 Conversion of Maleic Acid to MA Product
T-102 Product Purification

## Slide 18: n-butane to MA PFD Flowsheet
Stream |  | 1 | 2 | 5 | 7 | 8 | 9 | 11 | 12 | 13 | 14 | 15
Temp. (°C) |  | 20 | 20 | 410 | 45 | 59.9 | 60 | 120 | 120 | 160 | 97.1 | 162
Press. (kPa) |  | 275 | 101 | 275 | 170 | 170 | 170 | 101 | 101 | 101 | 101 | 101
Vapor Fraction |  | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0.7 | 0 | 0
Flowrate (kg/h) |  | 2000 | 41174 | 43174 | 11216 | 37621 | 16769 | 13640 | 3128.8 | 3128.8 | 602.5 | 2526.3
Component Flowrates (kg/h) |  |  |  |  |  |  |  |  |  |  |  | 
Nitrogen | -- |  | 31210 | 31210 | -- | 31210 | -- | -- | -- | -- | -- | --
Carbon Monoxide | -- |  | -- | 21.7 | -- | 21.7 | -- | -- | -- | -- | -- | --
Oxygen | -- |  | 9511 | 6287.4 | -- | 6287.4 | -- | -- | -- | -- | -- | --
Carbon Dioxide | -- |  | -- | 102.3 | -- | 102.3 | -- | -- | -- | -- | -- | --
Butane | 2000 |  | -- | 355.9 | -- | -- | 355.9 | 355.9 | 0.1 | 0.1 | 0.1 | --
Water | -- |  | 453 | 2491.2 | 11216 | -- | 2491.2 | 13206 | 12.6 | 496 | 491.5 | 4.5
Formic Acid | -- |  | -- | 17.8 | -- | -- | 17.8 | 17.6 | 0.2 | 0.2 | 0.2 | 0.1
Acrylic Acid | -- |  | -- | 27.9 | -- | -- | 27.9 | 26.6 | 1.4 | 1.4 | 0.6 | 0.8
Maleic Anhydride | -- |  | -- | 2659.6 | -- | -- | 2659.6 | -- | -- | 2631.2 | 110.2 | 2521
Maleic Acid | -- |  | -- | -- | -- | -- | -- | 33.6 | 3114.6 | -- | -- | --
Reactants
Waste
Products
Intermediates

## Slide 19
Stream | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Temp. (°C) | 20 | 20 | 147.9 | 121 | 410 | 95 | 45 | 59.9 | 60 | 40 | 120 | 120 | 160 | 97.1 | 162
Press. (kPa) | 275 | 101 | 275 | 275 | 275 | 200 | 170 | 170 | 170 | 101 | 101 | 101 | 101 | 101 | 101
Vapor Fraction | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0.7 | 0 | 0
Flowrate (kg/h) | 2000 | 41174 | 41174 | 41174 | 43174 | 43174 | 11216 | 37621.4 | 16768.5 | 16768.5 | 13639.7 | 3128.8 | 3128.8 | 602.5 | 2526.3
Component Flowrates (kg/h) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nitrogen | -- | 31210 | 31210 | 31210 | 31210 | 31210 | -- | 31210 | -- | -- | -- | -- | -- | -- | --
Carbon Monoxide | -- | -- | -- | -- | 21.7 | 21.7 | -- | 21.7 | -- | -- | -- | -- | -- | -- | --
Oxygen | -- | 9511 | 9511 | 9511 | 6287.4 | 6287.4 | -- | 6287.4 | -- | -- | -- | -- | -- | -- | --
Carbon Dioxide | -- | -- | -- | -- | 102.3 | 102.3 | -- | 102.3 | -- | -- | -- | -- | -- | -- | --
Butane | 2000 | -- | -- | -- | 355.9 | 355.9 | -- | -- | 355.9 | 355.9 | 355.9 | 0.1 | 0.1 | 0.1 | --
Water | -- | 453 | 453 | 453 | 2491.2 | 2491.2 | 11216 | -- | 2491.2 | 2491.2 | 13206 | 12.6 | 496 | 491.5 | 4.5
Formic Acid | -- | -- | -- | -- | 17.8 | 17.8 | -- | -- | 17.8 | 17.8 | 17.6 | 0.2 | 0.2 | 0.2 | 0.1
Acrylic Acid | -- | -- | -- | -- | 27.9 | 27.9 | -- | -- | 27.9 | 27.9 | 26.6 | 1.4 | 1.4 | 0.6 | 0.8
Maleic Anhydride | -- | -- | -- | -- | 2659.6 | 2659.6 | -- | -- | 2659.6 | 2659.6 | -- | -- | 2631.2 | 110.2 | 2521
Maleic Acid | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | 33.6 | 3114.6 | -- | -- | --

## Slide 20: Metrics from PFD for n-butane Process
20.5
Yield: R-101 Yield = 0.787 Overall Yield=
Additional Metrics:
Environmental Index, Cost Index, Effective Mass Yield, etc.
Environmental Persistence, Bioaccumulation, Bioconcentration, etc.
Others?
8
15
11
14

## Slide 21: Summary – Level 1
Metric | Benzene Process | Butane Process
Reaction |  | 
E-factor (MW) | 1.27 | 0.734
Atom Economy | 0.454 | 0.577
Environmental Index | 5.60 | 4.00
Yield | 0.62 | 0.468
Reaction Mass Efficiency | 0.122 | 0.270
Process (PFD) |  | 
E-factor (mass) | 7.5 | 8.18
Yield | 0.62 | 0.787
Reaction Mass Efficiency | 0.114 | 0.281
Environmental Index | 5.46 | 4.0
Notes: For Environmental Index of the Process, use 0.73 lbm benzene per 1 lbm of MA

## Slide 22: Questions and Discussion?
What are the benefits of Level 1 Metrics?
What are the shortcomings of Level 1 Metrics?
Can you propose a greener alternative for the MA synthesis?
  Succinic Acid  Succinic Anhydride  MA
  Use renewable energy sources
  Find a greener alternative for MA in consumer goods. MA itself has high toxicity.
  Inherently Safer Design.