## Slide 1: Green Engineering: Application of Metrics and the Presidential Green Chemistry Challenge Award
Level 2 Metrics Case Studies
Maleic Anhydride Production Scale

## Slide 2: Level 2 Metrics – Benzene to MA Process Example
Emissions from Process Units
Storage Tanks for Benzene, Crude MA, DBP
Reactor (R-501)
Scrubber Column (T-501)
Distillation Tower (T-502)
Feed Heater and Steam Boiler (H-501)
Fugitive Emissions from valves, pumps, heat exchangers, reboilers, etc.

## Slide 3: Benzene to MA PFD
1
4
Reactants
13
7
12
Conversion
Waste
Product
R.Turton, .C.Bailie, W.B.Whiting, and J.A.Shaeiwitz; Analysis, Synthesis and Design of Chemical Processes, 3/E ; Prentice Hall
11

## Slide 4: Level 2 Metrics – Benzene to MA Process Example
Production of 2597 kg/hr of Crude MA (94.7%)
Assume a basis of 1000 lbm of MA, which is 0.1845 hrs of operation
Storage Tanks
  Assume a 3 day turnover for benzene and crude MA, 1 month turnover for DBP tank
  (2597 kg/hr crude MA)
  = 4461 ft3/3 days
  Assume Verticle fixed roof tank w/ no pollution control, white color, good condition
  Tank 15 ft tall, 20 ft diameter = 4712 ft3
  From TANKS EPA software Total Emissions = 1/071 lbm/yr or 0.0226 lbm/1000 lbm MA

## Slide 5: Level 2 Metrics – Benzene to MA Process Example
Tanks (same type of tanks)
  Benzene /3 days
  Tank 16 ft tall, 28 ft diameter = 9852 ft3
  Emissions 8,492 lbm/yr or 0.1789 lbm/1000 lbm MA
  DBP
  Tank 7 ft tall, 12 ft diameter = 792 ft3
  Emissions 246 lbm/yr or 0.0052 lbm/1000 lbm MA

## Slide 6: Level 2 Metrics – Benzene to MA Process Example
Reactor
  Based on Reactor Outlet, Stream
  Emission Factor EF = 1.5 kg/1000kg throughput
  = 3.899
  Or
8

## Slide 7: Level 2 Metrics – Benzene to MA Process Example
Scrubber Off Gas sent to Incinerator
Assume all VOC in stream goes to CO2 and H2O
Neglect N2, O2, H2O
Total CO2 = 4215
12

## Slide 8: Level 2 Metrics – Benzene to MA Process Example
3. Emissions from Scrubber (Stream 11 ) w/ EF = 0.2
*Value is Unreasonably high due to low volatility
4. Emissions from Tower (Stream ) w/ EF = 0.1
, , ,
5. Fugitive Emissions w/o detailed PFD
Assume
11
11

## Slide 9: Level 2 Metrics – Benzene to MA Process Example
Energy Requirements
  For hp and lp steam, use recovered heat from exothermic Rxn.
  Feed Heater: Requires 26,800 MJ/hr
  For Natural Gas (table 8.3-6*) Fuel Value = 34 MJ/m3
  For uncontrolled small industrial boiler
  SO2
  NOx
  CO
  CO2
  *Allen and Shonnard, Green Engineering: Environmentally Conscious Design of Chemical Processes, 2001

## Slide 10: Level 2 Metrics – Benzene to MA
Summary
Emission Totals (lbm per 1000 lbm MA)
Neglecting N2, O2, H2O; Quinone and Maleic Acid are very low
Sodium Nitrite and Sodium Nitrate are ignored
Global Warming Potential GWPCO2=1 GWPNOx=40
+ ++
Acid Rain Potential
GWP and ARP primarily come from burning Natural Gas. ARP is low because Natural Gas is a clean burning fuel
MA | Benzene | DBP | CO2 | CO | SO2 | NOx
3.97 | 0.303 | 11.3 | 4917 | 0.432 | 0.003 | 0.504
Notes: Blue is Indirect GWP

## Slide 11: Level 2 Metrics – Benzene to MA
Summary – Comparison of Benzene process with n-butane process
The primary differences arise from using benzene vs. n-butane
Benzene (6 carbons) produces 2 CO2 per 1 MA, thus CO2 off gas is 2298 lbm vs. 93 lbm for n-butane
Benzene process produces quinone byproduct, which is small but requires excess O2 to minimize but leads to CO2 generation
Benzene emissions are likely close to n-butane based on volatility, but the difference in Environmental Index (Toxicity) is significant (8,492 lbm/yr benzene emissions is appreciable)
Notes: Blue is Indirect GWP