## Slide 1: Green Engineering: Application of Metrics and the Presidential Green Chemistry Challenge Award
Prof. Christopher Kitchens
Dept. of Chemical and Biomolecular Engineering
Clemson University

## Slide 2: What Is Green Engineering?
Definition: The Design, Commercialization, and Use of Processes and Products in a way that:
  Reduces Pollution
  Promotes Sustainability
  Minimizing the Risk to Human Health and the Environment
  Without sacrificing Economic Viability and Efficiency
  *US EPA - https://www.epa.gov/green-engineering/about-green-engineering#definition - 2016
Notes: This is a working definition from the EPA and updated from the prior definition in th Allen and Shonnard text. Key terms are the breath from conception to application (design to use) and includes both processes and products. The concepts apply to both Human Health and the Environment, so it is not all environmental but includes the safety of a workforce and consumer. In Green Engineering, everything also comes down to economics and efficiency. There has been nor will ever be a greener alternative that is implemented that is economically viable when looking at the big picture.

## Slide 3: The Dilemma and The Challenge
Global Population Growth has placed enormous pressure on world wide natural resources and strain on the natural environment
The Challenge of Chemical Engineers is to develop and master the tools and approaches that will integrate sustainability objectives into design decisions.

## Slide 4: The Dilemma and The Challenge
Sustainability, Green Engineering,
and the Triple Bottom Line (Triple P)
Environmental
Planet
Economic
Profit
Societal
People
Notes: It is important to note that all three are integral components and a key component of sustainability is the time dimention.

## Slide 5: Examples of People (and Companies) Solving the Challenge
The Presidential Green
Chemistry Challenge (PGCC) Award
Each year, the EPA awards up to six PGCC Award in the following areas:
  - Greener Synthetic Pathways - Small Business
  - Greener Reaction Conditions - Academic
  - Design of Greener Chemicals - Climate Change
In the first 20 years, the EPA presented 104 awards, recognizing groundbreaking scientific solutions to real-world environmental problems.
The 104 PGCC award-winning technologies have significantly reduced the hazards associated with designing, manufacturing, and using chemicals. Specifically, they have:
  Eliminated 826 million pounds of hazardous chemicals and solvents each year—enough to fill a train nearly 47 miles long.
  Saved 21 billion gallons of water each year—the amount used by 820,000 people annually.
  Eliminated 7.8 billion pounds of CO2 equivalents released each year—equal to taking 810,000 automobiles off the road

## Slide 6: Approach to Green Engineering
Begin with the First Realization that there is no truly “GREEN” Product or Process.
We can only make Products or Processes GREENER!
Simpler, Safer, More Efficient, Less Wasteful
Second Realization: No Greener alternative has ever been adopted that was not also economically beneficial.

## Slide 7: The Role of a Chemical Engineer
Traditional Methods
  Economic Analysis
  Process Optimization
  Recycle Streams
  Heat Integration
  Waste Treatment
In order to increase the sustainability of a given product or process, the impact on Human Health and the Environment must be minimized.
Emerging Green Methods
  Inherently Safer Design
  Design for the Environment
  Getting to Zero Waste
  Biomimicry
  Cradle to Cradle

## Slide 8
A practicing chemical engineer may say:
  “In my plant we strive for efficiency, recover and recycle solvents and reactants, recover waste heat, use catalysts, and minimize toxic releases to the environment …
  Are we not Green Engineers?
Reply: YES, These are aspects of Green Engineering that are driven by economics … Now ask yourself:
  What happens at the product’s end of life?
  Where are the raw materials sourced from?
  What happens when an accidental exposure or release does occur?
  Can you do better?
                YES, How can I do better?

## Slide 9: How do we evaluate how “Green” something is? Answer: Metrics
Green Chemistry Metrics
  A Metric is a quantifiable standard of measure that can be used for comparison.
  Green Chemistry Metrics can be used to:
  Determine if one product or process is “greener” than another. (Comparative)
  Identify aspects of a product or process that can be improved. (Improvement)
  Many GC Metrics exist. The challenge is to chose the most appropriate.

## Slide 10
Traditional Tools
Level 1
  Yield and Selectivity
  Raw Materials Cost
  Energy Requirements
  Product Price
  Waste Treatment
Level 2
  Process Optimization
  Process Integration
Level 3
  Process Design
  Sustainability Analysis
Green Chemistry Tools
Level 1
  E-Factor
  Atom Economy
  Effective Mass Yield
  Reaction Mass Efficiency
  Environmental Index
Level 2
  Routes to Exposure
  Hazard Assessment
  Risk Analysis
Level 3
  Life Cycle Assessment
  Sustainability Analysis

## Slide 11: Conventional Metrics
Cost Index
  Where is the stoichiometric or actual mass ratio with respect to the primary product
  is negative for reactants and positive for products
Reaction Yield for
  if A is the limiting reagent
Reaction Selectivity for
  Yield = Conversion x Selectivity
  With multiple reactions, maximizing selectivity and recycle of unreacted reagents to maximize yield.

## Slide 12: Green Chemistry Metrics
E-Factor
  Simple metric proposed by R. Sheldon in 1990’s
  Applicable to a single reaction or chemical process.
  Difficult to apply across industries.
  Does not designate the type of waste.
Industry | Product (Ton/yr) | E-Factor
Oil Refining | 106 - 108 | < 0.1
Bulk Chemicals | 104 - 106 | < 1 to 5
Fine Chemicals | 102 - 104 | 5 to > 50
Pharmaceuticals | 10 - 102 | 25 to > 1000
Nanotechnology | 10 - 102 | 25 to > 1000

## Slide 13: Green Chemistry Metrics
Atom Economy
  based on molecular weight (MW)
  Goal is to optimize atomic efficiency (larger is better)
  Simple metric, applicable to Chemical Reactions or Processes
  Does not account for Yield, Selectivity, Solvents and other workup materials, etc.

## Slide 14: Green Chemistry Metrics
3. Effective Mass Yield (EMY)
  Proposed by Hudlicky in 1999
  Simple metric, applicable to Chemical Reactions or Processes
  Somewhat accounts for the types of materials/chemicals used but definition of nonbenign can be difficult.

## Slide 15: Green Chemistry Metrics
4. Reaction Mass Efficiency (RME)
  Simple Metric that accounts for atom economy (AE), yield, stoichiometry and material recovery
  ε is the actual product produced (kg) divided by the theoretical maximum production with respect to the limiting reagent (kg).
  Stoichiometric Factor =
  Material Recovery Parameter =
    c, s, and w are the mass of the reaction catalyst, solvents, and workup materials.
    mP is the mass of desired product
  If catalyst is recycled (c = 0), if solvents are recovered (s = 0), if workup and purification materials are recovered (w = 0), if no excess reagents are used (SF = 1)
  Improved simple metric, but does not account for material toxicity

## Slide 16: Green Chemistry Metrics
5. Environmental Index (EI)
  Environmental
  Where is the stoichiometric or actual mass ratio with respect to the primary product
Threshold Limit Values (TLV) – Airborne Concentration per 8 hour workday or 40 hour work week level for which no adverse effects over the workers lifetime. Set by ACGIH – American Conference of Governmental Industrial Hygienists
Permissible Exposure Limits (PEL) – Set by OSHA – Occupational Safety and Health Administration. Are legally binding.
Recommended Exposure Limits (REL) – Set by NIOSH under CDC
For TLVs, PELs, and RELs; the higher the value the better.
Environmental Index ~ 1/TLV is a better relationship. The lower the better and greater distinction of toxic chemicals
Notes: For the Environmental index, the smaller the number the better or a small toxicity factor. For a TLV, PEL, or REL the larger the number, the safer the chemical, so for the inverse TF, the lower the better. Also, the inverse relationship is effective at discerning differences in toxicity. For example, a highly toxic and moderately toxic compound will have relatively small differences in their TLV but the inverse of the numbers will be large. Analogously, the TLV for two relatively non-toxic compounds may be quite, but the inverse of those values are not very different.
Drawbacks of TLVs, PELs, RELs, etc.
Lack of Toxicity Weighting – The slope of the toxic response curve in the low dose region. Can adjust with a slope factor (Can Show a Dose vs Response toxicity curve.).
Differences in Exposure Routes – Inhalation vs Ingestion, Oral Slope Factor

## Slide 17: Examples for Level 1 Metrics
Case Study on Ibuprofen
  1997 Presidential Green Chemistry Challenge Award Winner
Maleic Anhydride
  Reaction Level Metrics
  Process Level Metrics

## Slide 18: GC Metrics - Ibuprofen Example
Conclusions
By incorporating a catalyst, a 6 step process goes to 3 steps with greater Atom Economy from 40% to 77%.
Generally, each step involves a reaction followed by a separation; each of which has waste, requires materials and energy, etc.
Analysis can be expanded to include yields, workup materials, energy efficiency, toxicity analysis …

## Slide 19: Maleic Anhydride Summary – Level 1
Metric | Benzene Process | Butane Process
Reaction |  | 
E-factor (MW) | 1.27 | 0.734
Atom Economy | 0.454 | 0.577
Environmental Index | 5.60 | 4.00
Yield | 0.62 | 0.468
Reaction Mass Efficiency | 0.122 | 0.270
Process (PFD) |  | 
E-factor (mass) | 7.5 | 8.18
Yield | 0.62 | 0.787
Reaction Mass Efficiency | 0.114 | 0.281
Environmental Index | 5.46 | 4.0
Notes: For Environmental Index of the Process, use 0.73 lbm benzene per 1 lbm of MA

## Slide 20: Questions and Discussion?
What are the benefits of Level 1 Metrics?
What are the shortcomings of Level 1 Metrics?
Can you propose a greener alternative for the MA synthesis?
  Succinic Acid  Succinic Anhydride  MA
  Use renewable energy sources
  Find a greener alternative for MA in consumer goods. MA itself has high toxicity.
  Inherently Safer Design.

## Slide 21: Level 2 Metrics
Routes to Exposure
  Emissions from a Chemical Plant
  Environmental Fate
Hazard Assessment
  Toxicity
  Environmental Impact: Atmospheric Persistance, Aquatic half-life, Biodegredation Index, Bioaccumulation or Bioconcentration Factor, etc.
Risk Analysis
Risk = Hazard x Exposure

## Slide 22: Level 2 Metrics
Applies to Input/Output Flow Sheet w/ Preliminary Processes and Unit Operations. Eg. Storage Units, Reactors, Seperation Units, Mixers, Heaters, Piping etc.
Environmental Release Assessment
Obtain process flow sheet and identify waste and emission streams
Determine a method to evaluate release rate at each release point.
Determine data needed
Collect data (if existing process)
Quantify release rates and frequency; media to which release occurs
Document Release Assessment, include methods and uncertainties.

## Slide 23: Potential Sources of Release
Fugitive Emissions – leaks from valves, pumps, fittings, sampling connections etc.
Venting of equipment
Equipment cleaning and repair
Filling and Emptying of Transportation Containers
Incomplete Separations
Does not include known releases – Vent stacks, waste water treatment facility

## Slide 24: Potential Sources of Release
Emissions from Process Units and Fugitive Sources
E (mass/time) = mvoc*EFave*M
Mvoc = mass fraction
EFave = Emission Factor for each unit
(kg emitted / kg throughput)
M = mass flow rate
Emission factors for each specific unit and depends on type of fluid, valves, vents, gasket etc
Losses from Cleaning Drums and Tanks
Depends on size, shape, and material of tank
Depends on cleaning method and solution
Depends on the chemical properties, viscosity, solubility in the cleaning solution, volatility, etc.

## Slide 25: Fugitive Emissions
Eg. Hydrazine – Toxic, Carcinogen, Corrosive, Explosive, Toxic to aquatic species, etc.
1984 – US Production 30 million ibs
2005 – Arch Chemicals awarded 20 year, $149 million for production, storage, transport
2000 – Annual California industrial emissions estimated at 1664 lbs released to environment
Now, Find your own example (homework)
Lets Revisit the Maleic Anhydride Production

## Slide 26: Level 2 Metrics – Benzene to MA Process Example
Emissions from Process Units
Storage Tanks for Benzene, Crude MA, DBP
Reactor (R-501)
Scrubber Column (T-501)
Distillation Tower (T-502)
Feed Heater and Steam Boiler (H-501)
Fugitive Emissions from valves, pumps, heat exchangers, reboilers, etc.

## Slide 27: Benzene to MA PFD
1
4
Reactants
13
7
12
Conversion
Waste
Product
R.Turton, .C.Bailie, W.B.Whiting, and J.A.Shaeiwitz; Analysis, Synthesis and Design of Chemical Processes, 3/E ; Prentice Hall
11

## Slide 28: Level 2 Metrics – Benzene to MA
Summary
Emission Totals (lbm per 1000 lbm MA)
Neglecting N2, O2, H2O; Quinone and Maleic Acid are very low
Sodium Nitrite and Sodium Nitrate are ignored
Global Warming Potential GWPCO2=1 GWPNOx=40
+ ++
Acid Rain Potential
GWP and ARP primarily come from burning Natural Gas. ARP is low because Natural Gas is a clean burning fuel
MA | Benzene | DBP | CO2 | CO | SO2 | NOx
3.97 | 0.303 | 11.3 | 4917 | 0.432 | 0.003 | 0.504
Notes: Blue is Indirect GWP

## Slide 29: Level 2 Metrics – Benzene to MA
Summary – Comparison of Benzene process with n-butane process
The primary differences arise from using benzene vs. n-butane
Benzene (6 carbons) produces 2 CO2 per 1 MA, thus CO2 off gas is 2298 lbm vs. 93 lbm for n-butane
Benzene process produces quinone byproduct, which is small but requires excess O2 to minimize but leads to CO2 generation
Benzene emissions are likely close to n-butane based on volatility, but the difference in Environmental Index (Toxicity) is significant (8,492 lbm/yr benzene emissions is appreciable)
Notes: Blue is Indirect GWP

## Slide 30: Level 3 Metrics
Further Increasing Level of Complexity
More in-depth Flow sheet analysis
Examine Raw Material Sources, Waste Treatment, Product end of life, etc.
Life Cycle Assessment (see module)
Green Process Design (see module)
Green Product Design

## Slide 31: Examples for Level 3 Metrics
Presidential Green Chemistry Challenge Awards
  Battelle (2008 winner), Development and Commercialization of Biobased Toner
  Novozymes (2001 winner), BioPreparation of Cotton
  Bayer Corp. (2001 winner), Baypure™ CX (Sodium Iminodisuccinate): An Environmentally Friendly and Readily Biodegradable Chelating Agent

## Slide 32: Assignment: Assessment of the Presidential Green Chemistry Challenge Award Winners using Green Chemistry Metrics
The goal of this case study assignment is to evaluate the work that has received the Presidential Green Chemistry Challenge (PGCC) Award using green chemistry metrics, principles, and design strategies. (http://www2.epa.gov/greenchemistry/presidential-green-chemistry-challenge-winners)
In the first 20 years of the awards program, the EPA has presented 104 awards, recognizing groundbreaking scientific solutions to real-world environmental problems. The PGCC has significantly reduced the hazards associated with designing, manufacturing, and using chemicals. Specifically, the 104 award-winning technologies have:
  Eliminated 826 million pounds of hazardous chemicals and solvents each year—enough to fill a train nearly 47 miles long.
  Saved 21 billion gallons of water each year—the amount used by 820,000 people annually.
  Eliminated 7.8 billion pounds of CO2 equivalents released each year—equal to taking 810,000 automobiles off the road
For this assignment, your team will identify one winner of the PGCC Award. You will research the different award winners and choose your award according to the availability of information and merit of the award. The assignment has two parts.
The first part is to perform a critical review. Using information available on the EPA website, company website, press releases, sustainability reports, or any other resource, you must compile information into a written report. You are encouraged to use additional GC metrics or Princilples in your assessment.
The second part requires you to contact the award winners (by email, phone, in person, social media, etc.) and interview them based on 1) what the PGCC Award has meant to them and their career and 2) what personal benefit have they gained from working the award winning technology.
See attachment for details

## Slide 33: Take-home Message
First Realization: There is no truly “GREEN” Product or Process. You can only make Products or Processes GREENER!
Second Realization: No Greener alternative has ever been adopted that was not also ECONOMICALLY BENEFICIAL.
Metrics are used to measure how “GREEN” a product or process is.
Green Innovation is an opportunity for you to make a difference. You may be a future Presidential Green Chemistry Challenge Award Winner.

## Slide 34: Supplementary Concepts for Review
12 Principles of Green Chemistry
12 Principles of Green Engineering

## Slide 35: 12 Principles of Green Chemistry
Waste Prevention
Atom Economy
Less Hazardous Chemical Syntheses
Designing Safer Chemicals
Safer Solvents and Auxiliaries
Design for Energy Efficiency
Use of Renewable Feedstocks
Reduce Derivatives
Catalysis
Design for Degradation
Real-time analysis for Pollution Prevention
Inherently Safer Chemistry for Accident Prevention
*Anastas, P. T. and Warner, J. C. Green Chemistry: Theory and Practice. Oxford University Press: New York, 1998, p. 30. By permission of Oxford University Press.
Notes: Green chemistry is the design of chemical products and processes that reduce or eliminate the use and generation of hazardous substances.*
1. Prevention - It is better to prevent waste than to treat or clean up waste after it has been created.
2. Atom Economy - Synthetic methods should be designed to maximize the incorporation of all materials used in the process into the final product.
3. Less Hazardous Chemical Syntheses - Wherever practicable, synthetic methods should be designed to use and generate substances that possess little or no toxicity to human health and the environment.
4. Designing Safer Chemicals - Chemical products should be designed to effect their desired function while minimizing their toxicity.
5. Safer Solvents and Auxiliaries - The use of auxiliary substances (e.g., solvents, separation agents, etc.) should be made unnecessary wherever possible and innocuous when used.
6. Design for Energy Efficiency - Energy requirements of chemical processes should be recognized for their environmental and economic impacts and should be minimized. If possible, synthetic methods should be conducted at ambient temperature and pressure.
7. Use of Renewable Feedstocks - A raw material or feedstock should be renewable rather than depleting whenever technically and economically practicable.
8. Reduce Derivatives - Unnecessary derivatization (use of blocking groups, protection/ deprotection, temporary modification of physical/chemical processes) should be minimized or avoided if possible, because such steps require additional reagents and can generate waste.
9. Catalysis - Catalytic reagents (as selective as possible) are superior to stoichiometric reagents.
10. Design for Degradation - Chemical products should be designed so that at the end of their function they break down into innocuous degradation products and do not persist in the environment.
11. Real-time analysis for Pollution Prevention - Analytical methodologies need to be further developed to allow for real-time, in-process monitoring and control prior to the formation of hazardous substances.
12. Inherently Safer Chemistry for Accident Prevention - Substances and the form of a substance used in a chemical process should be chosen to minimize the potential for chemical accidents, including releases, explosions, and fires.
*Anastas, P. T. and Warner, J. C. Green Chemistry: Theory and Practice. Oxford University Press: New York, 1998, p. 30. By permission of Oxford University Press.

## Slide 36: 12 Principles of Green Engineering
1. Inherent Rather than Circumstantial
2. Prevention Instead of Treatment
3. Design for Separation
4. Maximize Efficiency
5. Output-Pulled Versus Input-Pushed
6. Conserve Complexity
7. Durability Rather than Immortality
8. Meet Need, Minimize Excess
9. Minimize Material Diversity
10. Integrate Material and Energy Flows
11. Design for Commercial "Afterlife"
12. Renewable Rather Than Depleting
* Anastas, P.T., and Zimmerman, J.B., "Design through the Twelve Principles of Green Engineering", Env. Sci. Tech. 2003, 37(5), 94A-101A.
Notes: Green Engineering is the development and commercialization of industrial processes that are economically feasible and reduce the risk to human health and the environment.*
12 Principles of Green Engineering*
1. Inherent Rather than Circumstantial - Designers need to strive to ensure that all materials and energy inputs and outputs are as inherently nonhazardous as possible.
2. Prevention Instead of Treatment - It is better to prevent waste than to treat or clean up waste after it is formed.
3. Design for Separation - Separation and purification operations should be designed to minimize energy consumption and materials use.
4. Maximize Efficiency - Products, processes, and systems should be designed to maximize mass, energy, space, and time efficiency.
5. Output-Pulled Versus Input-Pushed - Products, processes, and systems should be "output pulled" rather than "input pushed" through the use of energy and materials.
6. Conserve Complexity - Embedded entropy and complexity must be viewed as an investment when making design choices on recycle, reuse, or beneficial disposition.
7. Durability Rather than Immortality - Targeted durability, not immortality, should be a design goal.
8. Meet Need, Minimize Excess - Design for unnecessary capacity or capability (e.g., "one size fits all") solutions should be considered a design flaw.
9. Minimize Material Diversity - Material diversity in multicomponent products should be minimized to promote disassembly and value retention.
10. Integrate Material and Energy Flows - Design of products, processes, and systems must include integration and interconnectivity with available energy and materials flows.
11. Design for Commercial "Afterlife" - Products, processes, and systems should be designed for performance in a commercial "afterlife."
12. Renewable Rather Than Depleting - Material and energy inputs should be renewable rather than depleting.
* Anastas, P.T., and Zimmerman, J.B., "Design through the Twelve Principles of Green Engineering", Env. Sci. Tech. 2003, 37(5), 94A-101A.

## Slide 37: References
Allen, D. T.; Shonnard, D. R. (2001) Green engineering: Environmentally conscious design of chemical processes and products New Jersey: Prentice Hall.
Lapkin, A.; Constable, D. (Eds.) (2008) Green Chemistry Metrics: Measuring and Monitoring Sustainable Processes Wiley.
Jimenez-Gonzalez, C.; Constable, D. (2011) Green Chemistry and Engineering: A Practical Design Approach Wiley.
Turton, R.; Bailie, R. C.; Whiting, W. B.; Shaeiwitz, J. A. (2008) Analysis, Synthesis and Design of Chemical Processes 3rd Ed. New Jersey: Prentice Hall.
Anastas, P. T.; Warner, J. C. (1998) Green Chemistry: Theory and Practice New York: Oxford University Press.
Anastas, P. T.; Zimmerman, J. B.; Design through the Twelve Principles of Green Engineering. Environ. Sci. Technol. 2003, 37(5), 94A-101A.