## Slide 1: Sustainability Root Cause Analysis (SRCA)
Helen H. Lou, Professor
Dan F. Smith Department of Chemical Engineering
Lamar University

## Slide 2: Course Content
  SCRA Methodology
  Sustainability Assessment
    Economic
    Environmental
    Social
  Root Cause Analysis
    Pareto Analysis
    Fish Bone Analysis
  Combination Method of Sustainability Assessment and Root Cause Analysis known as Sustainability Root Cause Analysis (SCRA)
  Biodiesel Case Study

## Slide 3: SRCA in Sustainable Manufacturing
Why we need SRCA for Sustainable Manufacturing?
  A major challenge In Sustainable Manufacturing is to identify the bottleneck issues in order to improve its sustainability effectively.
What are the key outcomes from SRCA?
  The complicated cause-and-effect relationships in sustainability require a SCRA to identify the key actions towards effective sustainability improvement.
What are the major interpretations we can gain from SRCA for a manufacturing process?
  SCRA can visualize various relationships between seemingly disconnected elements, and screen out significant factors and correlations for sustainability improvement.

## Slide 4: Methodology Outline
Conduct Sustainability Assessment in economic, environmental and social aspects
Identify root causes in each aspect using Pareto Analysis
Create a relationship diagram for the major causes using Fish-bone Analysis

## Slide 5: Sustainability Assessment
Economic
Capital Costs
Operating Costs
Social
Chemical Safety
Process Safety
Environmental
Potential Impacts

## Slide 6: Sustainability Assessment: Economic Evaluation
The following three sub-indicators are used to measure the performance in the economic dimension
Profit
NPV (Net Present Value)
NPV = -CTCI + ∑ CA,m / (1+r)m
CTCI : Total capital investment before base year composed of total fixed capital cost, working capital cost
CA : Total annual income cash flow after base year m
r : The interest rate
x : The project life after base year
IRR/DPV (Internal Rate of Return/Discounted cash flow rate of return)
IRR = FV / (1+i)n = FV (1-d)
FV : The nominal value of a cash flow amount in a future period
i : The interest rate
d : The discount rate
n : The time in years before the future cash flow occurs
NPV and IRR taking into account the economic life cycle including initial investment, annual profit, annual depreciation, salvage value and interest on investment

## Slide 7: Sustainability Assessment: Environmental Impact
EPA WAR Algorithm:
Use the Potential Environmental Impacts (PEI) as the indicator
A low PEI score indicates a lower environmental impact
URL: http://www.epa.gov/nrmrl/std/war/sim_war.htm
Note: Developed by Young & Cabezas (EPA), 1999

## Slide 8
General Impact Category | Impact Sub-Category | Measure of Impact Category
Human toxicity | Ingestion | LD50
 | Inhalation/Dermal | OSHA PEL
Ecological toxicity | Aquatic toxicity | Fathead minnow LD30
 | Terrestrial toxicity | LD50
Global atmospheric impacts | Global warming potential | GWP
 | Ozone depletion potential | ODP
Regional atmospheric impacts | Acidification potential | AP
 | Photochemical oxidation potential | PCOP
Sustainability Assessment: Environmental Impact
WAR Algorithm: Impact Categories

## Slide 9
Sustainability Assessment: Environmental Impact
WAR Algorithm: Potential Environmental Impact (PEI)
The potential environmental impact balance is as follows:

## Slide 10
Sustainability Assessment: Social Criteria
The social aspect of sustainability is the most difficult to measure and it involves many soft criteria, which are based on human intuitive and it is normally influenced by the decision maker’s knowledge and experience.
Some of the commonly used sub-indicators are listed below:
  Relationship with local community
  Safety
  Number of jobs provided
  Wealth created per employee
  Equity

## Slide 11
Process
Inventory
Temperature
Pressure
Equipment
Chemical
Flammability
Explosiveness
Toxic Exposure
Corrosiveness
Sustainability Assessment: Social Criteria
For chemical manufacturing, social criteria is mainly about the degree of safety of the process
Suitable for early design stage
Safety Evaluation conducted by computing the Inherent Safety Index
Inherent safety is computed for Chemicals and Processes in the following categories

## Slide 12
Flammability, IFL | Score
Nonflammable | 0
Combustible (flash point > 55 C) | 1
Flammable (flash point <= 55 C) | 2
Easily flammable (flash point < 21 C) | 3
Very flammable (flash point < 0 C & boiling point <= 35 C) | 4
Explosiveness (UEL-LEL) vol%, IEX | Score
Non explosive | 0
0-20 | 1
20-45 | 2
45-70 | 3
70-100 | 4
Chemical Inherent Safety
Reference: Heikkila, A.M., Inherent Safety in Process Plant Design, An Index-Based Approach. 1999, Helsinki University of Technology: Helsinki.
Sustainability Assessment: Social Criteria
Toxic Limit (ppm), ITOX | Score
TLV > 10000 | 0
TLV <= 10000 | 1
TLV <= 1000 | 2
TLV <= 100 | 3
TLV <= 10 | 4
TLV <= 1 | 5
TLV <= 0.1 | 6
Corrosiveness, ICOR | Score
Carbon steel | 0
Stainless steel | 1
Better material needed | 2

## Slide 13
Process Inherent Safety
Inventory, II | Score
0-1 t | 0
1-10 t | 1
10-50 t | 2
50-200 t | 3
200-500 t | 4
Process Temperature, IT | Score
< 0 oC | 1
0-70 oC | 0
70-150 oC | 1
150-300 oC | 2
300-600 oC | 3
>600 oC | 4
Sustainability Assessment: Social Criteria
Process Pressure, IP | Score
0.5-5 bar | 0
0-0.5 or 5-25 bar | 1
25-50 bar | 2
50-200 bar | 3
200-1000 bar | 4
Equipment Safety, IEQ | Score
Equipment handling nonflammable, nontoxic materials | 0
Heat exchangers, pumps, towers, drums | 1
Air coolers, reactors, high hazard pumps | 2
Compressors, high hazard reactors | 3
Furnaces, fired heaters | 4

## Slide 14: Root Cause Analysis
Root cause analysis (RCA) aims at identifying the root causes of problems
The RCA works on the belief that problems are best solved by attempting to correct or eliminate root causes, as opposed to merely addressing the immediately obvious symptoms
The RCA methodology includes the Pareto analysis and Fish-bone diagram

## Slide 15: Root Cause Analysis : Pareto Analysis
  To screen out significant factors and correlations for sustainability improvement
  80/20 Rule: 80% of problems caused by 20% causes
Image source: dreamsonwings.blogspot.com

## Slide 16: Root Cause Analysis : Fish-bone Diagram
  To visualize various relationships, and convey the important relationships between seemingly disconnected elements
  In SCRA, the results of the Pareto analysis are used to prepare the Fish-Bone diagram, in order to represent the major causes which drive the process away from being sustainable.

## Slide 17: Sustainability Root Cause Analysis
  The first step is to conduct a sustainability evaluation based on economic, social and environmental criteria
  Then the Pareto analysis identifies the top causes for poor performance
  These are then systematically presented using a fish-bone diagram and each cause is analyzed to find means of improvement

## Slide 18: Case Study : Biodiesel Production
Source: http://sei.oregonstate.edu

## Slide 19: Biodiesel Production
Source: http://blogs.rsc.org
Conventional Biodiesel Process:
Uses homogeneous catalyst (NaOH)
NaOH forms an emulsion with glycerol, which complicates downstream processing

## Slide 20: The Conventional Homogeneous Process
Reference: Haas, M. J.; A. J. McAloon, W. C.Yee and T. A. Foglia. A Process model to estimate biodiesel production costs. Bioresource Technology 97(2006) 671-678

## Slide 21: The Conventional Homogeneous Process
  The free fatty acid (FFA) content of the triglyceride stock should be below 0.5 wt% for the alkali (NaOH) transesterification process to be efficient
    The presence of FFA competes with the transesterification reaction by consuming alkali to produce soaps and water
    This makes the transesterification reaction very slow, and causes emulsion formation
  NaOH forms emulsion with glycerol, which creates problems in the downstream processing and purification of biodiesel
  The catalysts are not re-usable

## Slide 22: Feed Streams and Conditions
Feed Streams | 
Oil (triolein) | 1050 kg/hr
Methanol | 121 kg/hr
NaOH | 44.5 kg/hr
H3PO4 | 34.2 kg/hr
Water | 50 kg/hr
Reaction Conditions | 
Temperature | 60 °C
Pressure | 4 bar

## Slide 23: Economic Evaluation
Parameters | Conventional Process
Total Capital Investment ($) | 8,247,978
Total Feedstock cost($) | 7,968,949
Total Utilities Cost ($) | 230,387
Total Waste management Cost ($) | 61,763
Total Labor Cost ($) | 1,510,080
Total Maintenance Cost ($) | 663,962
Total Operating Overheads ($) | 170,625
Property Taxes and Insurance Cost ($) | 164,960
Depreciation ($) | 412,398
General Expenses ($) | 362,604
Total Production Cost ($) | 11,545,728
Total Sales ($) | 12,086,807
Total Profit ($) | 541,079
Net Present Value ($) | (1,834,893)
Discounted Cash Flow Rate of Return (%) | 7

## Slide 24: Potential Environmental Impact
Chemical | Iout PEI/kg | Igen PEI/kg | Flow Rate, kg/hr | Iout PEI | Igen PEI
Methyl Oleate | 0.0609 | 0.0609 | 1051.4 | 64.04 | 64.03
Glycerol | 0.1150 | 0.1150 | 106.3 | 12.22 | 12.22
Triolein | 0.0015 | -0.0198 | 1050 | 1.56 | -20.79
Methanol | 0.0040 | -0.0359 | 117.2 | 0.47 | -4.21
Total | 0.1814 | 0.1202 | 2324.9 | 78.30 | 51.26
Chart: PEI output
| Methyl Oleate | Glycerol | Triolein | Methanol
Iout PEI | 0.0609 | 0.115 | 0.0015 | 0.004
Chart: PEI generated
| Methyl Oleate | Glycerol | Triolein | Methanol
Igen PEI | 0.0609 | 0.115 | -0.0198 | -0.0359

## Slide 25: Safety Evaluation
Inherent Safety Sub-indices | Symbol | Conventional Process
Chemical inherent safety index, ICI |  | 
Flammability | IFL | 2.6
Explosiveness | IEX | 0.2
Toxic exposure | ITOX | 11.7
Corrosiveness | ICOR | 0.1
Process inherent safety index, IPI |  | 
Inventory | II | 8
Process temperature | IT | 5
Process pressure | IP | 0
Equipment safety | IEQ | 14
TOTAL INHERENT SAFETY INDEX, ITI |  | 41.6

## Slide 26: Pareto Analysis: Economic
Equipment / Chemical / Utility | Description | Costs ($) | Percentage Effect on Economy (%) | Cumulative Percentage (%)
Oil | Chemical | 7526304 | 75.72 | 75.72
GLYCRCOL | Distillation Column | 395700 | 3.98 | 79.70
Methanol | Chemical | 364392 | 3.67 | 83.36
MEOHCOL | Distillation Column | 327300 | 3.29 | 86.66
ESTCOL | Distillation Column | 325000 | 3.27 | 89.93
Gas (Heating) | Utility | 227992 | 2.29 | 92.22
REACTOR | Reactor | 147900 | 1.49 | 93.71
NEUTR | Reactor | 135300 | 1.36 | 95.07
FILTER | Solid Separator | 118500 | 1.19 | 96.26
WASHCOL | Separator | 112800 | 1.13 | 97.40
B2 | Heat Exchanger | 75800 | 0.76 | 98.16
NaOH | Chemical | 74995 | 0.75 | 98.91
HX2 | Heat Exchanger | 22240 | 0.22 | 99.14
HX1 | Heat Exchanger | 22100 | 0.22 | 99.36
PUMP1 | Pump | 20300 | 0.20 | 99.56
PUMP2 | Pump | 20300 | 0.20 | 99.77
PUMP3 | Pump | 20300 | 0.20 | 99.97
Cooling Water | Utility | 2229 | 0.02 | 99.99
Electricity | Utility | 550 | 0.01 | 100.00

## Slide 27: Pareto Chart Economic
Chart: The Pareto Analysis - Economic Aspect
| Oil | GLYCRCOL | Methanol | MEOHCOL | ESTCOL | Gas (Heating) | REACTOR | NEUTR | FILTER | WASHCOL | B2 | NaOH | HX2 | HX1 | PUMP1 | PUMP2 | PUMP3 | Cooling Water | Electricity
Cause vs Percentage effect on economy | 75.7173 | 3.9809 | 3.6659 | 3.2928 | 3.2696 | 2.2937 | 1.4879 | 1.3612 | 1.1922 | 1.1348 | 0.76258 | 0.75448 | 0.22374 | 0.22233 | 0.20423 | 0.20423 | 0.20423 | 0.022426 | 0.0055324
Cause vs Cumulative Percentage | 75.7173 | 79.6982 | 83.3641 | 86.6569 | 89.9265 | 92.2202 | 93.7081 | 95.0693 | 96.2614 | 97.3962 | 98.1588 | 98.9133 | 99.137 | 99.3594 | 99.5636 | 99.7678 | 99.972 | 99.9945 | 100

## Slide 28: Pareto Chart: Economic
The oil price is dominant and contributes about 76% towards economic impacts.
If the oil cost is removed from the list, the impacts of other major factors can be seen.
In a similar manner, Pareto charts can be constructed for each dimension of sustainability.

## Slide 29: Pareto Analysis: Economic (Excluding Impacts of Oil)
Equipment / Chemical / Utility | Description | Costs ($) | Percentage Effect on Economy (%) | Cumulative Percentage (%)
GLYCRCOL | Distillation Column | 395700 | 16.39 | 16.39
Methanol | Chemical | 364392 | 15.10 | 31.49
MEOHCOL | Distillation Column | 327300 | 13.56 | 45.05
ESTCOL | Distillation Column | 325000 | 13.46 | 58.52
Gas (Heating) | Utility | 227992 | 9.45 | 67.96
REACTOR | Reactor | 147900 | 6.13 | 74.09
NEUTR | Reactor | 135300 | 5.61 | 79.69
FILTER | Solid Separator | 118500 | 4.91 | 84.60
WASHCOL | Separator | 112800 | 4.67 | 89.28
B2 | Heat Exchanger | 75800 | 3.14 | 92.42
NaOH | Chemical | 74995 | 3.11 | 95.52
HX2 | Heat Exchanger | 22240 | 0.92 | 96.45
HX1 | Heat Exchanger | 22100 | 0.92 | 97.36
PUMP1 | Pump | 20300 | 0.84 | 98.20
PUMP2 | Pump | 20300 | 0.84 | 99.04
PUMP3 | Pump | 20300 | 0.84 | 99.88
Cooling Water | Utility | 2229 | 0.09 | 99.98
Electricity | Utility | 550 | 0.02 | 100.00

## Slide 30: Pareto Chart Economic (Excluding Oil)
Chart: The Pareto Analysis - Economic Aspect
| GLYCRCOL | Methanol | MEOHCOL | ESTCOL | Gas (Heating) | REACTOR | NEUTR | FILTER | WASHCOL | B2 | NaOH | HX2 | HX1 | PUMP1 | PUMP2 | PUMP3 | Cooling Water | Electricity
Cause vs Percentage effect on economy | 16.3939 | 15.0968 | 13.5601 | 13.4648 | 9.4458 | 6.1275 | 5.6055 | 4.9095 | 4.6733 | 3.1404 | 3.1071 | 0.92141 | 0.91561 | 0.84103 | 0.84103 | 0.84103 | 0.092353 | 0.022783
Cause vs Cumulative Percentage | 16.3939 | 31.4908 | 45.0509 | 58.5157 | 67.9614 | 74.089 | 79.6945 | 84.6039 | 89.2773 | 92.4177 | 95.5248 | 96.4462 | 97.3618 | 98.2028 | 99.0438 | 99.8849 | 99.9772 | 100

## Slide 31: Pareto Chart Environment
Chart: The Pareto Analysis - Environmental Aspect
| Methyl Oleate | Glycerol | Triolein | Methanol
Cause vs Percentage effect on environment | 81.8143 | 15.6097 | 1.9827 | 0.59324
Cause vs Cumulative Percentage | 81.8143 | 97.4241 | 99.4068 | 100

## Slide 32: Pareto Chart Safety
Chart: The Pareto Analysis - Safety Aspect
| Distillation Column | FAME, Methyl Oleate | Oil, Triolein | Pump | Heat Exchanger | Reactor | Separator / Extractor | Methanol | Glycerol | H3PO4 | NaOH | Na3PO4 | Water
Cause vs Percentage effect on safety | 24.0563 | 15.1757 | 15.1555 | 12.0282 | 12.0282 | 12.0282 | 4.8113 | 1.9517 | 1.2777 | 0.72169 | 0.60141 | 0.16434 | 0
Cause vs Cumulative Percentage | 24.0563 | 39.232 | 54.3875 | 66.4156 | 78.4438 | 90.4719 | 95.2832 | 97.2349 | 98.5126 | 99.2343 | 99.8357 | 100 | 100

## Slide 33: The Fishbone Diagram

## Slide 34: The Top 20% Factors
Economic | 
Capital Cost | Heat Exchanger
 | Separator
 | Distillation Column
Operating Cost | Oil
 | Gas used for Heating
Safety | 
Equipment | Heat Exchangers
 | Reactors
 | Distillation Column
Chemicals | FAME
 | Oil
Environmental | 
Chemicals | FAME
 | Glycerol

## Slide 35: Strategies for Sustainability Improvement
Reduce the number of distillation columns and reactors.
Reduce/eliminate the consumption of methanol
Reduce/eliminate the generation of glycerol
Other solutions

## Slide 36: A Proposed Alternative Process

## Slide 37: A Heterogeneous Catalyst Process
Reference:
Jayswal, A., X. Li, A. Zanwar, H. H. Lou and Y. L. Huang, “A Sustainability Root Cause Analysis Methodology and its Application,” Computers and Chemical Engineering, 35(12), 2011, 2591-3048.

## Slide 38: Homogeneous vs. Heterogeneous Process
Heterogeneous Process
  Solid catalysts (i.e., Na2O, MgO) can be operated in continuous processes and they can be reused and regenerated
  The continuous transesterification of triglycerides and simultaneous esterification of free fatty acids with very low residence time was reported
  The catalysts don’t form emulsion with glycerol, which makes the downstream processing and purification steps easy
  A variety of less expensive feedstocks that often contain high levels of free fatty acids, such as tall oil, algae oil can be used
Reference:
1. McNeff, C.V.; McNeff, L.V.; Yan B.; Nowlan, D. T.; Asmussen, M..; Gyberg, A. E.; Krohn, B. J.; Fedie, R.L.; Hoye T.R. Continuous catalytic system for biodiesel production, Applied Catalysis 2008, 343, 39- 48
2. Singh, A. K.; Development of conventionally catalysed chemical process to produce biodiesel. MS Dissertation, Mississippi State University, Mississippi, 2008

## Slide 39: Homogeneous vs. Heterogeneous Process
Heterogeneous Process (A result of the SRCA of the homogeneous process)
  Uses fewer reactors and distillation columns compared to the conventional (homogeneous) process
  Reaction occurs at a lower temperature
  Uses fewer types and quantity of raw materials
  Detailed comparison
    Jayswal, A., X. Li, A. Zanwar, H. H. Lou and Y. L. Huang, “A Sustainability Root Cause Analysis Methodology and its Application,” Computers and Chemical Engineering, 35(12), 2011, 2591-3048
 | Conventional Process | Heterogeneous Process
Feed condition |  | 
Oil (triolein) | 1050 kg/hr | 1050 kg/hr
Methanol | 121 kg/hr | 114 kg/hr
NaOH | 44.5 kg/hr | 
H3PO4 | 34.2 kg/hr | 
Water | 50 kg/hr | 
Reaction condition |  | 
Temperature oC | 60 | 48
Press, bar | 4 | 4

## Slide 40: Conclusion
    SCRA is a valuable tool for sustainability enhancement.
    After sustainability assessment, SCRA uses the Fishbone Diagram for visualization of relationships and the Pareto Analysis method to screen out the factors that adversely affect the sustainability performance of the system.
    SRCA provides answers to the critical questions:
    Why a process’ sustainability performance is not good enough?
    Which aspects contribute most to the overall sustainability performance?
    Can we change any design elements to improve the overall system’s performance?

## Slide 41: Acknowledgement
The development of this module has been supported through funding from the US National Science Foundation, award number 1140000, award title: RCN-SEES: Sustainable Manufacturing Advances in Research and Technology (SMART) Coordination Network.