## Slide 1: Carbon Dioxide Utilization: Educational Module
By: Sherif Khalifa
Advisors:
Mahmoud El-Halwagi, Ph.D Debalina Sengupta, Ph.D

## Slide 2: Safety moment

## Slide 3: Safety moment
http://healthland.time.com/2012/01/20/the-hazards-of-using-headphones-while-you-walk/

## Slide 4: Presentation Outline
Introduction to Global Warming
Sustainability
Process Integration
Sustainability education
Educational Module
Case Study
Results
Conclusions
Challenges
Next Steps
Questions

## Slide 5: What is Global Warming?
Gradual increase in earth’s surface temperature due to the effect of greenhouse gas (GHG) emissions
GHG emissions include CO2, NOx, CH4 and CFC’s
GHG emissions in the lower atmosphere trap heat that would otherwise escape from earth
GHG emissions are produced from various human activities:
  Burning of fossil fuels
  Chemical Manufacturing
  Deforestation

## Slide 6: Impacts of Global Warming
Melting of Arctic ice
Flooding of many coastal cities and those at lower altitudes
Acidification of oceans
Extreme heat waves and droughts
Projected increase in annual average river runoff by 10-40% by 2050
Decline in Rain-fed agricultures of by as much as 50% by 2020
Spread of mosquito-borne and infectious diseases due to heat surges

## Slide 7: GHG Emissions statistics
According to U.S EPA, CO2 contributes 65% to global emissions and 81% to U.S emissions
CO2 comes mainly from fossil fuels and industrial operations
U.S is the second largest emitter after China
Carbon emissions are exponentially increasing due to increasing populations and higher energy demands
*Courtsey of Boden, T.A., Marland, G., and Andres R.J. (2015). Global, Regional, and National Fossil-Fuel CO2 Emissions.

## Slide 8: How to combat global warming?
Sustainability!
  U.S EPA defines sustainability as
  “Sustainability occurs when we maintain or improve the material and social conditions for human health and the environment over time without exceeding the ecological capabilities to support them” (Sidkar, 2003)
  Sustainable process design balances three principal objectives
  “triple bottom line: People, Planet, and Profit” (Elkington, 1994)

## Slide 9: Process integration as an approach to Sustainability
Process integration is defined as
“a holistic approach to process design, retrofitting, and operation that emphasizes the unity of the process” (El-Halwagi, 1997)
Process integration activities (El-Halwagi,2006)
  Task Identification- e.g reducing emissions or increasing profit
  Targeting-Identifying performance benchmarks
  Generation of Alternatives- Process synthesis
  Selection of alternatives- Finding optimal alternatives
  Analysis of selected alternatives- Evaluation of optimal solutions via process analysis
Process synthesis
Process Analysis

## Slide 10: Importance of teaching sustainability
From the report The Engineer of 2020, Visions of Engineering in the New Century
“It is our aspiration that engineers will continue to be leaders in the movement toward the use of wise, informed, and economical sustainable development. This should begin in our educational institutions and be founded in the basic tenets of the engineering profession and its actions.” (NAE, 2004)
Requirement of sustainability education in new engineering curricula
Well-rounded engineers who face the challenges of the 21st Century

## Slide 11: Educational Module: Objectives
Systematically develop a framework for selecting a profitable CO2 utilization process or a set of processes
Use optimization software and simulation package to find answers for several industrial scenarios
Follow series of guided activities to formulate an integrated and fully-developed profit maximization function
Account for gate to gate CO2 emissions in terms of dollars
Make educated well-reasoned decisions to maximize profit while utilizing as much CO2 as possible

## Slide 12: Educational Module: Structure
Seven activities of increasing complexities
Activities 1 and 2: benchmarking techniques
Activities 3 and 4: building an empirical profit maximization function
Activities 5-7: more complex factors in profit function

## Slide 13: Activity 1: Benchmarking profitability
Benchmarks are calculated by the Metric for Inspecting Sales and Reactants (MISR) ratios.
Ratios > 1.0 indicate profitability
CO2 is assumed free of charge in this activity
Activity Tasks:
Students are prompted to find the selling prices of the products and raw materials

## Slide 14: Activity 2: Effect of utilities
Modified MISR including utility costs
Where F is Annual flow
Student Tasks:
Calculate the heat of reaction at the specified operating conditions of each reaction (ASPEN PLUS Rstoic model)
Calculate the reactor utility cost
Reactor utility cost =
Calculate Modified-MISR ratios

## Slide 15: Activity 3: Material balance
Material balance equations act as constraints for the optimization model that would be built
Student Tasks:
Write the overall process mass balance equations
Write N-1 component mass balance equations, where N is the number of components of a given process
Writing N-1 would allow for more than one DOF (degree of freedom) for successful optimization
Assume 100% conversion (for simplicity!)

## Slide 16: Activity 4: Formulation of profit function
Building basic Profit maximization function along with mass balance constraints
Profit = Revenue from sales- cost of raw materials-Reactor utility cost
Profit=
Student Tasks:
Writing LINGO code with profit maximization function along with mass balance constraints.
Compare results with MISR and Modified-MISR ratios for validation
This activity introduces students to LINGO language

## Slide 17: Activity 5: Integrating plant utilities
Utility cost for all plant unit operations is taken into consideration in the profit function
Student Tasks:
Identify the unit operations from literature for a typical industrial process for each product (SRI reports, Technical Journals)
Estimate the heat duties of each unit, and calculate the plant utility cost
Modify the profit maximization function
Add capacity constraints
Compare with benchmark results

## Slide 18: Activity 6: Integrating Fixed capital investment (FCI)
Fixed capital investment is the money used to buy fixed capital e.g equipment, land, machinery, and pipelines
Student Tasks:
Find the capacity and FCI of a typical industrial process from literature
Calculate a-factor
Assume 10-year installment plan
Integrate FCI into the optimization model
Compare with MISR and Modified-MISR ratios

## Slide 19: Activity 7: Carbon credit & Carbon Social Cost
Carbon credit (CC) illustrates fixation of CO2, and Carbon Social Cost (CSC) represents the total CO2 emitted from the process and utilities (gate to gate)
Student Activities:
Find typical values of Carbon credit and Carbon Social Cost from literature
Assuming all utilities come from HP steam, calculate CO2 emission from steam generation
Calculate total carbon social cost
Calculate amount of CO2 being fixed
Modify profit function and run the code
Compare with MISR and Modified-MISR

## Slide 20: The optimization overview of CO2 utilization
Profit Objective function
Profit = Carbon Credit+ Gross Profit – Raw material cost –Plant Utilities –FCI –CSC
Equality Constraints
Mass Balance constraints
Total CO2 that has to be fixed
Inequality Constraints
Demand and Capacity
Non-zero logics

## Slide 21: Case Study: CO2 Exhaust from Ammonia Plant
U.S Largest Ammonia plant owned by CF industries located in Donaldsonville, LA
Production Capacity of NH3 is 1.74 MM tonnes per year
Estimated Annual CO2 emissions by EPA is 2.12 MM tonnes per year
New government regulations dictate reducing emissions or facing expensive CO2 tax
Government would credit the plant for every tonne of CO2 fixed
Chemical Engineers suggest the utilization of CO2 into value-added chemicals via various processing routes to maximize profit

## Slide 22: Case Study: Choosing products
Chemical Engineers need to carefully choose the value-added products and their respective processing routes
The products must be in high demand and profitable
The products must involve CO2 as a reactant
The processing routes should not incur high CO2 emissions
Analysis on previous criteria suggests the following products:
  Propylene Carbonate CO2 + C3H6O → C3H6CO3
  Phenol CO2 + C6H6 → C6H5OH + CO
  Benzoic Acid CO2 + C6H6 → C6H5COOH
  Ethylene Glycol CO2 + C2H4O → C2H4CO3
  C2H4CO3 + 2H2 → C2H4(OH)2 + CH3OH

## Slide 23: Benchmark results
Benzoic Acid process is suggested to be most profitable
Minimal effect of utility on Modified-MISR ratios

## Slide 24: Scenario 1: Effect of Carbon Credit and Carbon Social Cost
Carbon credit of $4/tone and CSC of $37/tone of CO2 is integrated in the profit function
Result for Capacity constraints: one plant for each product

## Slide 25: Scenario 1 cont’d: Effect of Carbon Credit and Carbon Social Cost
Result for locking capacity constraints: Choosing any process

## Slide 26: Scenario 2: Effect of Increasing utility cost of Propylene Carbonate
Setting UC of Propylene Carbonate (least expensive) to be equal to that of Ethylene Glycol (Most expensive). Eight times higher!
Result for Capacity constraints: one plant for each product

## Slide 27: Scenario 2 cont’d: Effect of Increasing utility cost of Propylene Carbonate
Result for locking capacity constraints: Choosing any process

## Slide 28: Scenario 3: Effect of increasing CSC
Stanford suggests CSC could be up to $220/tone of CO2 emitted
Result for Capacity constraints: one plant for each product

## Slide 29: Scenario 3 cont’d: Effect of increasing CSC
Result for locking capacity constraints: Choosing any process

## Slide 30: Conclusions
In this case study Benzoic Acid is most profitable
Results match those predicted by MISR ratios
Utility costs minimally contribute to profit
Profit is more sensitive to selling prices and demands
Based on this case study It is more profitable to fix CO2 rather than to emit it
Full capacity is reached

## Slide 31: Challenges
Finding up-to-date selling prices is difficult
Plant utility costs are outdated (1998 data)
No industrial process uses CO2 processing route yet
Lack of updated market demand information
Difficulty in obtaining realistic operating cost information
No integration between the processes

## Slide 32: Next Steps
Contact a chemical vendor or obtain up-to-date chemical pricing reports.
Obtain updated demand reports
Allow more than one plant to be built for each product to fix more CO2
Synthesize a process for each product given the processing route
Mass Integration
Heat Integration
Incorporating operating costs and transportation

## Slide 33: References
National Academy of Engineering (NAE) 2004. The Engineer of 2020: Visions of Engineering in the New Century, The National Academies Press, Washington, DC.
Halwagi M. M. 2012, “Sustainable Design Through Process Integration: Fundamentals and Applications to Industrial Pollution Prevention, Resource Conservation, and Profitability Enhancement”. ISBN 978-1-85617-744-3.
Peter U. Clark et al.: Consequences of twenty-first-century policy for multi-millennial climate and sea-level change. Nature Climate Change 6, 2016, 360-369, doi:10.1038/NCLIMATE2923
Battisti, David; Naylor, Rosamund L. (2009). "Historical warnings of future food insecurity with unprecedented seasonal heat". Science 323 (5911): 240–4.
Stavins, Robert N. (November 2001). "Experience with Market-Based Environmental Policy Instruments" (PDF). Discussion Paper 01-58 (Washington, D.C.: Resources for the Future). Retrieved 2010-05-20. Market-based instruments are regulations that encourage behavior through market signals rather than through explicit directives regarding pollution control levels or methods.
Al Bredenberg, March 2012. “Carbon Dioxide -- How Can One Little Molecule Be Such a Big Troublemaker?”. Web article. Link:http://news.thomasnet.com/imt/2012/03/06/carbon-dioxide-how-can-one-little-molecule-be-such-a-big-troublemaker.

## Slide 34: Thank you & Gig’em!

## Slide 35: Questions?

## Slide 36: Backup:

## Slide 37: Backup:

## Slide 38: Backup:

## Slide 39: Backup: